## Slide 1
INTERIM ASSESSMENT · 28 OCTOBER 2026
GAPPLER
High-Readiness Mobile Manipulation via Gaze-Speech Interaction and Continuous Pre-Alignment
Look at it, name it, and the robot fetches.
Dion · Sherman · Zongzhe
Supervisors: Prof Xie Lihua, Dr Yuan Shenghai

## Slide 2
PART 1 / 3 · WHY IT MATTERS
For older people, the hard part is getting there
Stay put. Look at it, ask for it.
1 in 4
Singapore citizens aged 65+ by 2030
NPTD, Population in Brief 2025
1 in 5
seniors aged 65+ fall each year
HealthHub, Ministry of Health
Problem and plan
Results
Where we stand
AT HOME · THE BOX IS ROOMS AWAY
She stays seated, looks at the box and asks. The robot makes the trip.
Illustration (AI-generated)

## Slide 3
GAPPLER · DION
THE BIG PICTURE
The BIG Picture
Someone looks at an object and names it. The robot does the rest.
ROBOT'S ROOM
YOUR ROOM
can't see your room
starting spot
you, in smart glasses
your box
look-alike
1
You look and ask
“get me the box”
2
Robot comes over
from another room
3
Searches the room
where you can see
Your box?
is it the one you looked at
4
Picks it up
with its arm
Brings it to you
later, beyond this project
yes
no: keep looking
5

## Slide 4
GAPPLER · DION
THE OBJECTIVE
Find, reach and grasp the object the user looked at
A new system, built on two published ones
FAM-HRI · LAI ET AL., 2025
Gaze and speech from the glasses tell a table-mounted arm what to pick
ASSUMES
The object is unobstructed, in front of the arm (fixed to table)
Fixed cameras: the wrist camera sees what the user sees
HICO-NAV · XU ET AL., ICRA 2026
Explores an unseen room and remembers each object's 3D position and image feature
ASSUMES
Finding is enough: no grasping, speech is the only input
“Find a box” returns any box, not the one you looked at
MILESTONES, EACH WITH A WRITTEN TEST (APPENDIX A10)
M1
Arm picks something up
M2
Voice and gaze reach the arm
M3
Base navigates
M6
Memory graph
M7
HiCo-Nav steers the search
M8
Gaze picks the instance
M11
Orchestrator runs every phase
M12
Base parks within reach
M10
Demo and paper
Evaluation: end-to-end trials, success per phase. Also M0, M4, M5 and M9.
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
4

## Slide 5
GAPPLER · ZONGZHE
THE SYSTEM
The target system works in five phases
From a spoken word and a glance to a grasp, in a room the robot has not seen
Obtain user prompt from speech and target object from gaze
›
Explore and map room, remembers objects and finds user
›
Match stored objects to the target object, output object list and their positions ranked by confidence
›
Drive close to the possible item, wrist camera verifies, repeat until target object verified
›
Choose, plan and execute the grasp if verified
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
5
INTENT CAPTURE
EXPLORE AND MAP
SEARCH
APPROACH AND CONFIRM
GRASP
WHAT IT IS
WHAT IT IS
WHAT IT IS
WHAT IT IS
WHAT IT IS

## Slide 6
GAPPLER · SHERMAN
OUR APPROACH
Open-source parts, plus what was missing
Every phase starts from published work we reviewed. Below each tool is what we added
INTENT CAPTURE
Aria SDK, SAM 3
WE ADDED
A gaze vote picks one object
RESULT · SLIDE 8
›
EXPLORE AND MAP
FAST-LIVO2,
HiCo-Nav graph
WE ADDED
Three port bugs fixed, graph written fresh
RESULT · SLIDE 9
›
SEARCH
HiCo-Nav, CLIP,
Qwen2.5
WE ADDED
Sentence to object classes, with a fall-back
RESULT · SLIDE 13
›
APPROACH AND CONFIRM
CLIP
WE ADDED
Glasses-to-wrist match, after keypoints failed
RESULT · SLIDE 14
›
GRASP
AnyGrasp,
MoveIt 2
WE ADDED
Grasp filters, safe state machine, stop
RESULT · SLIDE 15
BETWEEN THE PARTS
The gaze match
joins the two papers
Clear ownership
one owner for every connection
One step at a time
two people at the robot
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
6

## Slide 7
MOBILE BASE · FAST-LIVO2 MAP
Inside the lab map. Orange: the 26 m hand-pushed path.
PART 2 / 3
Results, phase by phase
Every stage measured on real hardware or real recordings
Problem and plan
Results
Where we stand

## Slide 8
GAPPLER · DION
PHASE 1 · INTENT CAPTURE
Speech gives the word, gaze picks the object
A one-second gaze vote over SAM 3 masks makes the reference crop sent to the robot
PHASE 1
Voice
one word per sentence
Gaze
streams simultaneously
Segment
SAM 3 finds every “box”
Vote
gaze picks a mask, then crop it
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
8
“Find the box.”
Speech detector
waits until you finish
Whisper
audio to text
Small language model
pulls out the object name
box
1
2
3
4
RIGHT BOX, STEADY STARE
60 of 61
recorded frames, at 1.4 to 2.4 m
3 of 4
spoken words at 4 different locations with varying depth and angles found correct crop
LIMIT
Hard to maintain gaze at fixed point for a long time and gaze estimation errors.

## Slide 9
GAPPLER · DION
PHASE 1 · INTENT CAPTURE
Speech gives the word, gaze picks the object
A one-second gaze vote over SAM 3 masks makes the reference crop sent to the robot
PHASE 1
Voice
one word per sentence
Gaze
streams simultaneously
Segment
SAM 3 finds every “box”
Vote
gaze picks a mask, then crop it
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
9
Eye cameras
track your pupils
Gaze point
where you are looking
The gaze point is placed on the RGB image from the glasses, shown here.
2
1
3
4
RIGHT BOX, STEADY STARE
60 of 61
recorded frames, at 1.4 to 2.4 m
3 of 4
spoken words at 4 different locations with varying depth and angles found correct crop
LIMIT
Hard to maintain gaze at fixed point for a long time and gaze estimation errors.

## Slide 10
GAPPLER · DION
PHASE 1 · INTENT CAPTURE
Speech gives the word, gaze picks the object
A one-second gaze vote over SAM 3 masks makes the reference crop sent to the robot
PHASE 1
Voice
one word per sentence
Gaze
streams simultaneously
Segment
SAM 3 finds every “box”
Vote
gaze picks a mask, then crop it
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
10
SAM 3 PROMPT “BOX” · ONE MASK AND SCORE PER BOX
Word
“box”
Image
from when you spoke
SAM 3
segmentation model
Masks
every box, with a score
Many boxes in one frame. Which one did the user mean? Next: the gaze vote
3
1
2
4
RIGHT BOX, STEADY STARE
60 of 61
recorded frames, at 1.4 to 2.4 m
3 of 4
spoken words at 4 different locations with varying depth and angles found correct crop
LIMIT
Hard to maintain gaze at fixed point for a long time and gaze estimation errors.

## Slide 11
GAPPLER · DION
PHASE 1 · INTENT CAPTURE
Speech gives the word, gaze picks the object
A one-second gaze vote over SAM 3 masks makes the reference crop sent to the robot
PHASE 1
Voice
one word per sentence
Gaze
streams simultaneously
Segment
SAM 3 finds every “box”
Vote
gaze picks a mask, then crop it
RIGHT BOX, STEADY STARE
60 of 61
recorded frames, at 1.4 to 2.4 m
3 of 4
spoken words at 4 different locations with varying depth and angles found correct crop
LIMIT
Hard to maintain gaze at fixed point for a long time and gaze estimation errors.
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
11
1.0 M · BOX PICKED
1.5 M · GAZE ON THE MATS
Blue ring: gaze vote window. The mask closest to the gaze point wins the vote.
Tested on recordings and replay. Live stream still throttled.
4
1
2
3

## Slide 12
GAPPLER · SHERMAN
PHASE 2 · EXPLORE AND MAP
A 3D map that closes within 12 mm
FAST-LIVO2 fuses LiDAR, IMU and colour camera into one 3D pose
PHASE 2
1
3D SLAM
2
Sensor Calibration
Hand-pushed 26 m loop, 20 Oct. Orange = path, ring = start and end.
LOOP CLOSURE
12 mm
back to start after 26 m
6.7 cm
worst error mid-route
11–14 ms
per frame on CPU (budget 100)
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
9
LIMIT
Pushed by hand, not yet driven by Nav2
NEXT STEPS
Nav2 drives it. The memory graph picks where to explore

## Slide 13
GAPPLER · SHERMAN
PHASE 2 · EXPLORE AND MAP
One link left to calibrate, and the graph depends on it
Each missing calibration blocks a specific later step
PHASE 2
1
3D SLAM
2
Sensor Calibration
LIMIT
Base camera not yet calibrated
NEXT STEPS
Calibrate on a target, check by overlaying LiDAR points
Mobile base
LiDAR
Base camera
Wrist camera
Arm
User + glasses
1
2
3
4
done
part way
planned
1
Base to arm
Measured
Arm and base agree on where things are
2
Wrist camera to arm
Calibrated
A grasp the camera sees, the arm can reach
3
Glasses to robot
Planned
Gaze picks between identical objects
4
Base camera to LiDAR
Mount measured, not calibrated
Gives each object its depth in the graph
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
10

## Slide 14
GAPPLER · ZONGZHE
As the robot drives, it builds a memory of objects
Each object gets a 3D position and a CLIP image feature, built from the recorded drive
PHASE 3
1
Build memory
2
Check accuracy
3
Search memory
LIMIT
Built offline from a recorded drive. Not yet live while driving
ONE KEPT PHOTO, FRAME 700
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
11
HOW THE GRAPH IS BUILT
Keep a photo
every 1 m or 45°
Find objects
SAM 3
Place in 3D
LiDAR depth
Describe
CLIP feature
Merge repeats
mostly by position
29 of 3,536
photos kept
5.7× faster
30 classes in one SAM 3 pass
How accurate these are: Check accuracy, two slides on
PHASE 3 · SEARCH

## Slide 15
GAPPLER · ZONGZHE
As the robot drives, it builds a memory of objects
Built once from the drive, then asked for every new prompt
PHASE 3
1
Build memory
2
Check accuracy
3
Search memory
LIMIT
Built offline from a recorded drive. Not yet live while driving
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
12
1 BUILDING THE GRAPH
Recorded photos
29 kept from the drive
Objects in 3D
each with a CLIP feature and position
2 ANSWERING A PROMPT
User prompt
“find the box”
Ranked list
of objects and their positions
MEMORY GRAPH
chair
table
box
Anchor: kept photo + camera pose
Object: 3D box, CLIP feature, class
PHASE 3 · SEARCH

## Slide 16
GAPPLER · ZONGZHE
Three changes keep the graph accurate when building it
Each one departs from HiCo-Nav and is measured on the lab drive
PHASE 3
1
Build Memory
2
Check Accuracy
3
Search Memory
LIMIT
Two drives, 16 objects: a difference of one is noise
DUPLICATES AT 10 CM
8 3
with no false merges
Why not merge by look?
Same chair
0.93
Same-model chairs
0.81–0.85
Other objects
0.56
CLIP image similarity, 0 to 1
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
12
1
Noise Filters
LiDAR sees the floor through a chair's gaps
Prevents objects from being mapped to backgrounds or floors
floor → seat
chair centre height,
−0.02 → 0.58 m
2
One pixel, one object
Graph decides merges based on overlap
Removing overlaps prevents wrong merges
5.4 % → 0
pixels in two masks
3
Determining merges
Graph needs to balance between minimising duplicates and preventing wrong merges
At 15 cm, wrong merges occur
Duplicates by radius (cm)
8
2.5
4
5
4
7.5
3
10
3
15
2
20
PHASE 3 · SEARCH

## Slide 17
GAPPLER · ZONGZHE
PHASE 3 · SEARCH
The robot then asks its memory where to go
Today the query is a sentence. In the full system, the gaze crop is the query (M8)
PHASE 3
1
Build Memory
2
Check Accuracy
3
Search Memory
LIMIT
Full query on the recorded drive not run yet: T6.8, weeks 7 to 8
1
LLM determines target object’s class based on prompt
“Find the chair”
›
chair
table
desk
2
Obtain prompt embedding
4
Return 2 ranked lists with respective 3D positions
Target classes first, related classes second, each by score. Each hit has a 3D centre and its best photo. A wrong hit can be rejected.
SENTENCE TO CLASSES
20 of 22
test instructions, checked by hand
BY LANGUAGE MODEL
Qwen2.5 1.5B (used)
20/22
No model, fallback
15/22
Qwen2.5 0.5B
12/22
0.28 to 0.32 s per reply, on the lab machine
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
13
3
Keep objects of target or related class, and rank by cosine similarity with prompt embedding

## Slide 18
GAPPLER · DION
PHASE 4 · APPROACH AND CONFIRM
Keypoints fail across cameras. CLIP picks the right box
Which wrist-camera mask is the object in the glasses crop?
PHASE 4
1
Method
Selection
2
Grasp Loop
LIMIT
A wrong gaze crop gives a wrong match (the mats at 1.5 m)
NEXT STEPS
Glasses refuse weak gaze picks before sending a crop
GLASSES CROP
WRIST CAMERA
Are they the same box?
Different camera, angle and distance
THE QUESTION
KEYPOINTS
CLIP Image Embedding
Matches land on the ceiling and floor
Right box in every pair
CLIP RANKS THE BOX FIRST
25 of 25
glasses vs wrist pairs, whole-object image features
BOX RANKED FIRST, BY METHOD
Keypoints
0 of 15
SAM 3 + text
7 of 25
SAM 3 image
15 of 25
CLIP image
25 of 25
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
17

## Slide 19
GAPPLER · DION
PHASE 4 · APPROACH AND CONFIRM
In the grasp loop, the arm goes for the box you looked at
CLIP now picks the grasp target, not SAM 3's most confident mask
PHASE 4
1
Method Selection
2
Grasp Loop
LIMIT
Identical boxes: 6 of 12. Appearance alone can't separate them
NEXT STEPS
Run it on the real arm, then add the gaze ray in the robot's frame
1
Target
glasses mask the user looked at
2
Candidates
every wrist-camera mask
3
CLIP
crop and embed each mask
4
Compare
cosine to the target
5
Pick best
over 0.56, no tie
otherwise the arm waits
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
14
0.97
TWO LOOK-ALIKE BOXES
0.98
THREE DIFFERENT BOXES
TWO LOOK-ALIKE BOXES
266 of 268
wrist targets on the box you looked at. The old pick got 0 of 114
334 of 334
three different boxes. Old pick: 105 of 115
2 misses
both from a wrong gaze crop

## Slide 20
GAPPLER · DION
PHASE 5 · GRASP
The real arm grasps on a spoken command
First real grasp on 13 Oct 2026, with a tested software stop
THIS PART
1
Live Grasp
2
AnyGrasp
3
Challenges
LIMIT
Fixed grasp orientations with dynamic positioning
NEXT STEPS
A learned model proposes the grasp
Idle
checks request
› Approach
steps to 30 cm
› Grasp
close and lift
› Hold
until “release”
13 OCT · REAL ARM
GRASPS BY DISTANCE
44.5 cm
4 of 4
49.5 cm
1 of 2
54.5 cm
out of reach
0 of 2
● grasped ○ failed · one dot per attempt, started by a recorded voice command
WITHIN REACH
5 of 6
grasps succeeded when target was within reach (5 of 8 overall).
< 1 ms
software stop cancels motion
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
15

## Slide 21
GAPPLER · DION
PHASE 5 · GRASP
AnyGrasp proposes grasps from one point cloud
One depth view in, hundreds of ranked grasps out, with no training on our box
THIS PART
1
Live Grasp
2
AnyGrasp
3
Challenges
LIMIT
Box in one orientation only
NEXT STEPS
Generalize to different box orientation x positions
WRIST VIEW
SAM 3 MASK
ARM + PROPOSED GRASPS
RViz on the real arm at the 30 cm stop. Point cloud is drawn as a rainbow, coloured by depth, Grasp candidates in green.
BOX IN ONE PLACE · REAL ARM
3 of 4
grasps held, box not pushed
HOW IT PICKS A GRASP
1
Stop at 30 cm one 3D snapshot
2
SAM 3 mask this object, within 10°
3
Propose grasps ranked by confidence
4
Stay best grasp for 5 frames then commit
5
Motion Planner IK solve, collision-free path
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
16
6
Line up, go in 10 cm out, straight in

## Slide 22
GAPPLER · DION
PHASE 5 · GRASP
The grasps work at one spot. Four problems limit the rest
Found on the real arm on 26 Oct 2026
THIS PART
1
Live grasp
2
AnyGrasp
3
Challenges
NEXT, CHEAPEST FIRST
A
Check reach first
B
More view angles
C
Fuse several views
D
Test 12 positions
WRIST CLOUD UP CLOSE · FRONT AND TOP ONLY
Real arm, 26 Oct. C is built, still to test.
FOUR CHALLENGES
1
One face visible
AnyGrasp guesses the hidden sides
front + top
2
Out of reach
steeper angles the arm can't reach
0 of 5
3
Late updates
box position arrives late
2–4 s
4
Edge grasps
landed near the box's edge
1 miss
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
17

## Slide 23
BASE CAMERA + LIDAR · NOT YET CALIBRATED
Two sensors, one scene: the parts work, the joins come next.
PART 3 / 3
Where we stand
Joins, schedule, budget and next steps
Problem and plan
Results
Where we stand

## Slide 24
GAPPLER · SHERMAN
WHAT WAS BUILT
Each of us built a working piece. Four joins remain
Green links work today, grey ones are wired but not yet run. Orange links are still to build
1 Intent
2 Explore
3 Search
4 Confirm
5 Grasp
Dion
intent to grasp
Zongzhe
memory and search
Sherman
map and driving
glance crop, on replay
recorded drive
Voice + gaze crop
tested on replay
Wrist camera check
best candidate selected
Grasp on real arm
tested on the real arm
Memory graph
works alone, offline
Find the object
CLIP search, built
FAST-LIVO2 map
built from recording
Nav2 drives base
built, not driven
gaze target
where to look
match → goal
arrive, check
works today
wired, not yet run
still to join
tested
works alone
In progress
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
18

## Slide 25
GAPPLER · SHERMAN
SCHEDULE
Ahead on memory and gaze, behind on driving
Final dates unchanged
exams, break
Oct
Nov
Dec
Jan
Feb
Mar
Apr
Sep
Build and run
Arm picks something up
Voice and gaze to arm
Base navigates
Closed loop
Calibrated base camera
Memory graph offline
HiCo-Nav steers the search
Gaze picks the instance
Semantic vs nearest-first
Demo and paper
Orchestrator, all phases
Park within arm reach
first full run
today
done
forecast
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
19

## Slide 26
GAPPLER · ZONGZHE
BUDGET AND COMPUTE
SGD 1,500 for compute, approved
Where compute fell short, we cut scope instead of solving it
APPROVED · 5 OCT 2026
1,500 SGD
both items for compute
1,000
500
Hardware GPU
API credits
WHY: ONE SHARED 16 GB GPU
10.3 GiB: batched SAM 3 alone
16 GB
Also AnyGrasp, CLIP, Whisper, 2 language models: 3 people + CI
COMPUTE LIMIT
WHAT WE DID INSTEAD
1
The paper's 8B vision-language model does not fit beside SAM 3
Small local Qwen2.5-1.5B, text only: right class for 20 of 22
2
SAM 3 on every camera frame is too slow
Segment one photo per 1 m or 45° moved: 29 of 3,536 frames
3
32 phrases in one SAM 3 pass run out of memory
16 per pass: 40 phrases in 1.69 s, peak 10.3 GiB
4
All the models never fit on the card at once
Each part is tested alone, one bench run at a time
WHAT WE COULD NOT AFFORD
A dedicated RTX 3090 with 24 GB: room for an 8B model next to SAM 3, off the shared lab card
3090, new
~2,800
3090, used
1,100–1,500
GPU budget
1,000
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
21

## Slide 27
GAPPLER · ZONGZHE
NEXT STEPS
Next: close the grasp, drive the base, query the graph
Then explore with gaze, to end-to-end trials in March 2027
1
Problem
System
Intent
Explore
Search
Confirm
Grasp
Plan
21
NAVIGATE TO OBJECT
RECLARIFICATION NODE
END-TO-END TESTING
ORCHESTRATION LAYER
2
3
4
Drive to the object and park within reach
One node decides what happens next
Ask the user when the request is unclear
• An LLM loop: search the graph, list candidates, ask
• Ends with one object or a lead, at most 3 questions
• Asked by phone. It never moves the robot
Success counted per phase
• First run: speak, look, drive, grasp
• Planted failures: does the right recovery fire?
• Trials with look-alikes, then a recorded demo
• The graph's position becomes the approach goal
• Park where the arm can reach the object
• The wrist camera re-finds it from above
• Each phase reports an outcome and a reason
• On failure: next candidate, second view, or ask
• The only node that starts motion

## Slide 28
MOBILE BASE · TOP VIEW OF THE LAB
Backup slides A1 to A10 follow.
THANK YOU
Questions
Look at it, name it, and the robot fetches that one.
Dion · Sherman · Zongzhe
Backup: wiring, frames, matching, grasp options, map accuracy, limitations, plan, evaluation.
Problem and plan
Results
Where we stand

## Slide 29
BACKUP · NOT IN THE 20 MINUTES
Appendix
WHOLE SYSTEM
A1
Topic-level wiring today
A2
Coordinate frames
A6
Limitations, risks, failures
A7
September plan vs now
A9
End-to-end evaluation plan
A10
Milestone tests
A15
What we inherited, what we fixed
GAZE, MATCHING AND GRASP
A3
Matching rule and thresholds
A4
Grasp filters, five options
A8
Why gaze, not a class name
A11
The grasp sequence, step by step
A12
Matching across cameras
A13
What narrows grasp candidates
A14
Gaze at the moment of speech
MAP AND MEMORY GRAPH
A5
FAST-LIVO2 defects, accuracy
A16
Our graph vs HiCo-Nav's code
A17
The photo gate: 29 photos
A18
LiDAR depth, occlusion filter
A19
Answer key, match radius sweep
A20
How the graph is tested
A21
Sentence to classes check
A22
Why a 24 GB card would help
A23
Reclarification node (planned)

## Slide 30
GAPPLER · APPENDIX
BACKUP · A1
A1 Topic-level wiring today
Answers: “What exactly is connected?” Only links that exist in code. Grey rows exist but have not run
Source: COMBINED_PROGRESS_REPORT_2026-10.md §3.3
24
From | To | Channel | State
Voice: Silero VAD, faster-whisper, Qwen2.5-0.5B | aria_segmentation_client | /aria/audio/prompt (String) | Ran (replay)
Eye model | aria_segmentation_client | /aria/eye_tracking/gaze_estimate | Ran (recording)
aria and grasp segmentation clients | SAM 3 service (one copy on GPU) | /segmentation/segment | Ran
aria_segmentation_client | grasp_segmentation_client | /grasp/target: word, then word plus reference crop | Ran on replay (T8.9a)
aria_segmentation_client | grasp_state_machine | /manipulator/grasp_request | Ran
grasp_segmentation_client | grasp_state_machine | /object_centroid_2d (pixel plus depth) | Ran
anygrasp_detection_node | grasp_state_machine | /grasp_candidates | Ran
grasp_state_machine | MoveIt and rm_driver | real arm | Ran on the real arm
Livox MID-360, base D455 | FAST-LIVO2, then fastlivo_odom_bridge | odom to robot_base_link | Ran live
fastlivo_odom_bridge | SLAM Toolbox, mapping mode | map to odom, /map | Ran live
SLAM Toolbox | Nav2 | frame tree | Never run on this
object_recognition_pipeline | object_approach_node | /manipulation/goal_pose (call commented out) | Not run
object_approach_node | Nav2 | /goal_pose | Not run
Recorded drive handdriven1 | Memory graph S0 to S13, then TargetFinder | offline | Graph built. Query not run

## Slide 31
GAPPLER · APPENDIX
BACKUP · A2
A2 Coordinate frames
Answers: “How do grasp poses reach the arm?”
Source: COMBINED_PROGRESS_REPORT_2026-10.md §6.7, §5.4
25
map
›
odom
›
robot_base_link
›
base_link
›
Link1 to Link6
›
camera_link
›
camera_color_optical_frame
plus livox_frame under robot_base_link
Parent to child | Published by | Value or note
map to odom | SLAM Toolbox | Nav2 plans in this map frame
odom to robot_base_link | Wheel driver, or the FAST-LIVO2 bridge (odom_source:=fastlivo) | Bridge: T_odom_base(t) = Tb x P0^-1 x P(t) x Tb^-1, Tb = (0.191, 0.02329, 0.15588) m. Refuses to start above 2° start tilt
robot_base_link to base_link | Static (arm mount) | (0.18, 0, 0.48) m, yaw 180°. Measured, tf2_echo matched
robot_base_link to livox_frame | Static | LiDAR mount
base_link through Link1 to 6 to camera_link | URDF | Wrist camera to arm calibrated (Dion, 24 Oct)
camera_link to camera_color_optical_frame | RealSense driver | AnyGrasp candidates arrive in this frame
Open question for P2 and T7.1: the memory graph stores positions in FAST-LIVO2's camera_init frame, while Nav2 drives in SLAM Toolbox's map frame. How graph positions reach map at run time is a design question, not a defect.

## Slide 32
GAPPLER · APPENDIX
BACKUP · A3
A3 Matching rule and thresholds
Answers: “Why 0.56? Is CLIP cosine a probability?”
Source: COMBINED_PROGRESS_REPORT_2026-10.md §5.4, §6.4, §6.6
26
THE RULE
Cosine between each wrist mask crop (box plus 20 px) and the reference crop. Cutoff 0.56, tuned on 20 pairs (T8.7). Masks within 0.01 of the best count as a tie, and a tie returns no match. Same model in both places: open_clip ViT-B-32 laion2b_s34b_b79k.
NOT A PROBABILITY
CLIP cosine is not calibrated. Thresholds are empirical: 0.56 for the matcher, 0.6 on the graph's 1.5 x overlap + 0.5 x appearance score. float16 shifts a vector by up to 0.0039 across batch sizes. Crop padding differs between glasses, wrist and graph.
Where | Method | Confidence handling
Glasses mask | Gaze vote | Winner needs half the votes, else word only
Wrist mask (matcher) | CLIP cosine | Cutoff 0.56, wrist tie returns no match
Wrist mask (grasp) | CLIP cosine when a reference exists (T8.9a), else SAM 3 score | Cutoff 0.56 and no tie, else nothing published
Graph association | 3D overlap plus CLIP | Score over 0.6, greedy
Graph query | CLIP text vs image | Ranking only
No stage carries a confidence forward to the next (see A6).

## Slide 33
GAPPLER · APPENDIX
BACKUP · A4
A4 Grasp filters and the five options
Answers: “Why not just lower the score floor?”
Source: COMBINED_PROGRESS_REPORT_2026-10.md §5.5. Options: DION_PROGRESS_REPORT_2026-10.md §7
27
FILTERS ON EVERY CANDIDATE
On the SAM 3 mask
Inside the approach cone
Score at least 0.3
Width under 68 mm
Fingertips at most 45 mm past the near face
Pose stable for 5 frames
Of the 180° twins, the smaller wrist turn (T1.33)
Option | Idea | Cost
A. Grasp from the view pose | AnyGrasp once at 0.4 to 0.5 m with the whole box in view, one planned motion | Small, the pieces exist
B. Fused views (T1.47) | Several views in one cloud, grasp on that | Built, retest owed
C. New AnyGrasp SDK (T1.45) | Native mask and angle steering | Waiting on licence
D. Closed-loop tracking | AnyGrasp's tracking mode updates the grasp while the arm moves | Medium, old node parked
E. Two-phase (shelved, T1.33) | Stop just before the depth blind zone, set the angle, move straight in and close | Small
WHY THE FLOOR IS NOT THE FIX
The top-down grasp scores at most 0.25, but the problem is the view. The 30° cone around the camera axis dropped every top-down grasp, because the camera axis is 44° from vertical. AnyGrasp was also used against its README: masked points only, 0.10 m width.

## Slide 34
GAPPLER · APPENDIX
BACKUP · A5
A5 FAST-LIVO2 port defects and mid-route accuracy
Answers: “How do you know the map is right?”
Source: COMBINED_PROGRESS_REPORT_2026-10.md §8.4. SHERMAN_PROGRESS_REPORT_2026-10.md §9.3, §11.4, §11.5
28
Defect (found by reading the source, confirmed against a control run) | Before | After the fix
Range gate cannot act (F2): blind_sqr never assigned, the port dropped upstream's line | Median 19,968 points per scan, the full packet | Median 9,607. Removed 52.06 % against 51.84 % audited zero-range points
LiDAR to IMU offset has the wrong sign (F3) | About 10.2 cm of geometric inconsistency in every replay before 19 Oct | Configs carry (-0.011, -0.02329, 0.04412) m. handdriven1 recorded after the fix
Voxel key mismatch: insertion and retrieval round negative coordinates differently | Key hits 1,392,458 vs 1,878,707 shadow hits | Hits match, 1,855,269. Retrieval points 112,980 to 128,385
MID-ROUTE ACCURACY (T3.5F)
Within 6.7 cm (run 1) and 6.5 cm (run 2) for the whole route, against the handdriven1 map, 0.15 s lag removed. The reference carries about 7 cm of its own error.
The mapper stamps its pose about 0.15 s late: surfaces smear about 4 cm at 0.28 m/s. Fix prepared, off by default.
Floor marks did not close as ground truth. A tape-measured check is owed.

## Slide 35
GAPPLER · APPENDIX
BACKUP · A6
A6 Limitations (1 of 3): confirmed in the code
Answers: “What fails today?” Most are links the plan schedules for later milestones
Source: COMBINED_PROGRESS_REPORT_2026-10.md §9.1. T7.1, T11.2, T12.3 in task-tree.html
29
Limitation | End-to-end implication
A wrong gaze pick becomes a confident reference (at 1.5 m the reference was the mat) | The arm would go for the wrong box. T2.24 refuses weak gaze picks
/manipulation/goal_pose has no live publisher (inherited) | Nothing can start navigation to an object yet. T7.1, the ApproachObject action, will call Nav2 directly
No graph query service, no T7.1 node | The graph cannot drive the robot
No gaze-target trigger on graph objects | The exploring robot cannot tell it has found the target. Glasses vs base-camera features untested
Graph built offline from a hand-pushed recording | No live graph. No depth camera data
No calibration between any cameras | Graph positions and the gaze ray carry unknown rotation error, about 6.7 px per degree
Software-only stops on arm and base | Every hardware test needs two people and the power button
No automatic grasp success check | Outcome judged by people. Planned: the grasp reports an outcome (T11.2) and the wrist checks the target (T12.3), so the orchestrator knows when to retry

## Slide 36
GAPPLER · APPENDIX
BACKUP · A6
A6 Limitations (2 of 3): risks when the parts join
Answers: “What could break when the parts join?”
Source: COMBINED_PROGRESS_REPORT_2026-10.md §9.3
30
Risk | What to watch
No confidence crosses a stage boundary | A wrong gaze pick gives a confident reference, a wrong graph hit a goal, a wrong wrist mask a grasp. The matcher caught one by luck of score (0.51 vs 0.56)
Crop mismatch | Fixed 20 px glasses crop against the graph's relative padding, when the gaze match (P3) lands
Frame of graph positions | camera_init against Nav2's map frame, to settle when P2 and T7.1 are built
Standoff vs reach | 0.6 m camera standoff against the 35 to 46 cm tested grasp band
GPU contention | SAM 3 service, batched graph SAM 3 (up to 10.3 GiB), AnyGrasp, CLIP, Whisper, two Qwen models on one 16 GB card. Never run together
0.15 s pose lag | Anything pairing a scan with a pose by stamp, including graph depth
Viewpoint change between graph and wrist | Graph features from the base camera, reference from the glasses, confirmation from the wrist. Glasses to base camera untested

## Slide 37
GAPPLER · APPENDIX
BACKUP · A6
A6 Limitations (3 of 3): observed failures
Answers: “What has gone wrong on hardware or data?”
Source: COMBINED_PROGRESS_REPORT_2026-10.md §9.2. Lab visitors' faces appear in the coloured map: re-render before any external showing
31
Failure | Where | Source
AnyGrasp's confident grasps go across the too-wide face. Fit check passes edge slices | Wrist, 0.21 m | T1.44
Live OK-Robot trials 0 of 4: one pushed the box, two stuck, one found nothing in 3 s | Real arm | T1.44
Wrist spun 180° and knocked the box off (fixed) | First AnyGrasp grasp | T1.33
Wide wrist twist (j4 146°, j5 29°, j6 274°) | AnyGrasp grasp B | T1.40
Look-alike boxes: 148 of 180, and 6 of 12 | Matcher | T8.5, T8.8
Gaze landed on the mat stack at 1.5 m | Glasses | T8.5
Keypoint matching 0 of 15 | Cross camera | T8.4
Mapper teardown aborts 2 of 4. LiDAR driver SIGBUS | Base | S§10.3
Ethernet flap caused 8.1 s and 15.1 s IMU time jumps | Base, live | T3.5d
Lab box silent hangs (6 Oct, 20 Oct) | Shared box | S§15
Glass walls: about 42 % of 5 cm map points are ghosts outside the glass box | Map | S§15
Glass door and both computer towers missed in every graph setting | Graph | Z§3.5

## Slide 38
GAPPLER · APPENDIX
BACKUP · A7
A7 September plan vs now
Answers: “How does this compare with your original plan?”
Source: 1cde0ec:docs/PROJECT_PLAN.md §5 and §6 headings. COMBINED_PROGRESS_REPORT_2026-10.md §0.2, §0.6
32
Milestone | September plan window | Now (actual to 24 Oct, forecast end) | Change
M0 Everyone can build and run | 14 to 27 Sep 2026 | Done 24 Sep | On time
M1 The arm picks something up | 5 Oct to 1 Nov 2026 | Started 21 Sep. Forecast 8 Nov | About one week later (AnyGrasp)
M2 Voice and gaze reach the arm | 26 Oct 2026 to 3 Jan 2027 | Started 8 Oct. Forecast 10 Jan | Started early, ends about a week later
M3 The base navigates | 12 Oct to 27 Dec 2026 | Started 14 Sep. Forecast 10 Jan | Two weeks later
M4 Closed loop | 28 Dec 2026 to 17 Jan 2027 | Forecast 11 to 31 Jan | Two weeks later
M5 Calibrated base camera | 5 Oct 2026 to 17 Jan 2027 | Started 16 Sep. Forecast 24 Jan | One week later
M6 Memory graph offline | 28 Dec 2026 to 7 Feb 2027 | Started 21 Sep. Forecast 31 Jan | One week earlier
M7 The graph drives the robot | 1 to 28 Feb 2027 | Forecast 18 Jan to 28 Feb | Can start earlier, end unchanged
M8 Gaze picks the instance | 8 Feb to 14 Mar 2027 | Started 19 Oct. Forecast 14 Mar | Started early, end unchanged
M9 Frontier scoring (optional) | 2 Nov 2026 to 21 Feb 2027 | Not started. 18 Jan to 21 Feb if kept | First on the cut list
M10 Demonstration and paper | 1 to 21 Mar 2027 | Forecast 1 to 21 Mar | Unchanged

## Slide 39
GAPPLER · APPENDIX
BACKUP · A8
A8 Why gaze, not just a class name
Answers: “Isn't identical-object picking niche?”
Source: COMBINED_PROGRESS_REPORT_2026-10.md §0.3 (D§5.5). CLIP values: §8.5
33
Two identical objects are the hardest test case, not the pitch. The capability is knowing where the user is looking in the robot's own 3D space.
Similar objects
Two chairs of the same model score 0.81 to 0.85 in CLIP, close to the same chair at 0.93
Partly hidden objects
The robot may see only part of the object the user sees
Uncertain image features
Appearance alone is not a reliable identity
A robot that does not see what the user sees
The base camera is at knee height, the glasses at eye level
Assistive use
A user who can look but cannot easily point or speak, among mugs, pill bottles and cans

## Slide 40
GAPPLER · APPENDIX
BACKUP · A9
A9 End-to-end evaluation plan
Answers: “How will you measure the final system?” Today every measurement is per stage
Source: COMBINED_PROGRESS_REPORT_2026-10.md §11. Recovery row: PROJECT_PLAN.md §5.1, M11
34
Metric | Definition | Needs | Milestone
Glasses target accuracy | Reference crop is the intended object, scenes with 2 to 4 objects at 1 to 3 m | Live glasses | M2
Wrist confirmation accuracy | Matcher picks the intended object, with and without look-alikes. Refusals counted apart | P0 item 1 | M2
False acceptance rate | Wrong object accepted, per stage (glasses, graph, wrist) | Labelled trials | M2, M8
Graph target retrieval | First hit lands on the intended marked object, and distance to it | T6.8 | M6
Gaze-target trigger accuracy | The robot stops exploring at the intended object. Wrong stops counted | T8.2 | M8
User discovery and search distance | User found, and distance driven before the target is matched | T7.5, T7.6 | M7
Without gaze (stretch) | Same trials, voice only | T8.11 | M8
Drive-to-point repeatability | Ten drives, landing error, 10 cm circle | T3.6, T5.8 | M3
Handover success | Base stops with the object inside the grasp band | T3.7 | M4
Grasp success | 12-trial grid, pass bar 9 of 12 | T1.35 | M1
End-to-end success | Speak, look, drive, grasp. Counted only when the intended object is lifted | All above | M4, M10
Per-stage timing | 99th percentile per stage | T4.2 | M4
Recovery | Share of failures that end safely instead of a wrong grasp | T11.10 | M11

## Slide 41
GAPPLER · APPENDIX
BACKUP · A10
A10 Milestone tests
Answers: “How do you know a milestone is done?”
Source: COMBINED_PROGRESS_REPORT_2026-10.md §0.2. PROJECT_PLAN.md §5.1 (M11, M12)
35
 | Milestone | Done means | Lead
M0 | Everyone can build and run | Two people other than Dion clone, build and pass the bench | Zongzhe
M1 | Arm picks something up | 5 grasp attempts on a box, success rate recorded, stop verified first | Dion
M2 | Voice and gaze reach the arm | Two boxes, the arm picks the one you looked at, 3 times in 4 | Dion
M3 | Base navigates | Map, localisation, ten drives to a point with error recorded | Sherman
M4 | Closed loop | One recorded run: speak, look, drive, grasp, per-stage timing | Dion
M5 | Calibrated base camera | LiDAR points land on the right objects in the camera image, pose error as a number | Sherman mount, Dion calibration
M6 | Memory graph offline | Objects from a recorded drive, no duplicates, a sentence query returns the right one | Zongzhe
M7 | Graph drives the robot | Object out of view: the robot explores, finds the user, builds the graph live, drives to it | Dion
M8 | Gaze picks the instance | A gaze match ends exploration. N end-to-end trials, success per phase | Dion
M9 | Smarter exploration order (optional) | The paper's exploration order beats our nearest-first exploration | Zongzhe
M10 | Demonstration and paper | Recorded end-to-end run, paper whose central table is the end-to-end trials | All
M11 | Orchestrator runs every phase | Each phase returns an outcome and a reason. Every failure in the table gets its response. Clarification ends in one object or a lead | Dion, Zongzhe clarification
M12 | Base parks within arm reach | Parks inside the measured reach, the wrist re-finds the object from above, the arm grasps | Sherman, Dion wrist look

## Slide 42
GAPPLER · APPENDIX
BACKUP · A11
A11 The grasp sequence, step by step
Answers: “What does the arm do after it hears a command?”
Source: grasp/grasp_state_machine/src/grasp_state_machine.cpp (workerLoop), grasp/grasp_config.yaml
37
1
Wait
IDLE
For a grasp request and the object's position from the wrist camera
2
Go home
HOME
Clear the old target, move the arm to its home pose
3
Approach
SELECTING
Step 2 cm at a time toward the object until it is 30 cm away
4
Grasp
EXECUTING
Open the gripper, wait for a steady grasp, plan the path and move in
5
Hold
HOLD
Close the gripper, move to the hand-over pose, wait for “release”
After “release”: open the gripper, go home, wait for the next command
WHEN A STEP FAILS, BACK TO WAIT
Approach: the object's position is over 7 s old, so the object counts as lost
Grasp: no grasp holds steady for 25 s
Grasp: 5 grasps in a row could not be planned. Each failed one is skipped next time
STOP, AT ANY STEP
A stop key halts the arm at once and drops the request
Nothing moves again until a person resumes it, then the sequence restarts at Wait

## Slide 43
GAPPLER · APPENDIX
BACKUP · A12
A12 Matching the looked-at object across cameras
Answers: “How does the robot know which box the user meant?”
Source: grasp/grasp_segmentation_client/cross_camera_mask_match_rule.py, aria/aria_config.yaml. Scores: three-box replay, 20 Oct 2026
38
1 · USER'S GLASSES
SAM 3 masks with their confidence. The ring is the gaze
SAM 3 finds every object matching the spoken word
Gaze votes for 1 s: each gaze sample votes for the mask under it, or the nearest within 80 px
The winner needs half the votes. Its cut-out is the reference sent to the robot
2 · MATCHER
CLIP turns the reference and each wrist mask into a feature vector. Cosine similarity compares them: 1 means they look the same
SCORES, THREE-BOX SCENE
Match
0.632
Other mask
0.623
Other mask
0.249
0.56
TWO RULES, ELSE THE ARM WAITS
Minimum score 0.56. Below it, no wrist mask matches
Tie margin 0.01. Two masks this close to the best are a tie, so no match (identical boxes)
3 · ROBOT'S WRIST CAMERA
0.98
Candidate masks. Orange: matched (detection 0.98)
SAM 3 finds candidates for the same word
Kept if detection confidence is 0.5 or more, at most 5
The match guides the approach and grasp
+- 0.01

## Slide 44
GAPPLER · APPENDIX
BACKUP · A13
A13 What narrows the grasp candidates
Answers: “Why was a grasp rejected?” Each box can remove or restrict candidates
Source: anygrasp_detection_node.py, anygrasp_to_grasp_frame.py, grasp_state_machine.cpp, mtc_planner.cpp, grasp_config.yaml
39
INPUTS
Depth image from the wrist camera
The object's outline from SAM 3
The arm's joint angles
Settings: approach within 10°, gripper opens 71 mm
GRASP SUGGESTER
AnyGrasp node
Scene cut to 15 cm around the object
AnyGrasp: grasps on the object only, within 10° of the camera's view
Collision check: the gripper may not hit the table or neighbours
Near-duplicates merged, best 5 kept
Fit check: object at most 68 mm wide, fingertips at most 45 mm in
Twin choice: of two mirror-image wrist turns, the one nearer the gripper
DECIDER
Grasp state machine
Approach at least 20° above horizontal (parallel to table)
Grasps that already failed to plan are skipped
Same best grasp for 5 frames, within 15 mm and 10°
Object position under 7 s old while approaching
Gives up after 25 s or 5 failed plans
MOTION PLANNER
MoveIt
Pre-grasp 10 cm in front: joint angles solved (IK) from the current joints
Path around obstacles, the box included
The straight move in must finish completely
Wrist guard: joints 4 to 6 turn at most 90°
Arm moves

## Slide 45
GAPPLER · APPENDIX
BACKUP · A14
A14 Sampling the gaze at the moment the user spoke
Answers: “How do you know where the user looked when they said the word?”
Source: aria_segmentation_client.py, aria/aria_config.yaml, stamped-word branch (T2.21, PR open). Gaze Pick Timing page
40
-2 s
-1 s
0 s
+1 s
+2 s
+3 s
+4 s
User says
Gaze
Images
Reaches robot
Client
gaze window
pick up the
box
the word is stamped with when it was said
segmented: nearest the window's middle
word arrives: 0.7 s of quiet ends the sentence + speech-to-text processing latency
waits up to 3 s if gaze or the image is late
decides, then SAM 3 and the vote
1.0 s Gaze window
starts this long before the word, ends at the word's end
gaze_before_word_s
3.0 s Wait for late data
for gaze up to the word's end and an image from the window
matching_image_wait_s
0.5 s Valid Voters
Only gaze taken within 0.5 s of the segmented image votes, so it matches what that image shows
gaze_to_image_max_s
80 px Vote reach
a gaze sample votes for the mask under it, or the nearest this close
pick_radius_px
50 % Winning share
below it, no pick: the word alone stands
vote_min_share
Every sample is placed by when the glasses captured it, not when it reached the robot.
Processing ideally ends here

## Slide 46
GAPPLER · APPENDIX
BACKUP · A11
A15 What we inherited, and what we fixed
Answers: “What did you add beyond the earlier team's code?”
Source: Gappler docs/CODE_AUDIT.md (audit of main @ 2d36a89, Sept 2026), task-tree.html, bench-runs/. Status as of 27 Oct
36
FOUND IN THE AUDIT
62 findings
Line-by-line read of the inherited code. No tests, no CI
27 fixed
or closed, with evidence
STILL OPEN
Voice “stop” halts the base, not the arm (B3). Return leg lands 2 m off (E1). 9 more in the audit
Area | What we inherited | What we did, and the evidence | Task
Grasp | No grasp could reach the arm: AnyGrasp ran only when idle, the state machine took grasps only when executing (A1 to A3) | Gate fixed. Replay 41 grasp sets while executing, 0 idle. AnyGrasp path now grasps on the real arm | T1.8, T1.17
Grasp | Arm moved as if the box were not there, curved into it and pushed it away (A4) | Box added to the planning scene, straight final approach. 3 of 3 grasps, first plan, no push | T1.48
Safety | E-stop lost its stop message (0 to 5 of 5 trials), ignored Ctrl+C, dropped fast keys. Launcher promised a “q” stop that did not exist (B1, B2) | Every stop path checked on the bench. Launcher text corrected | T1.2
Safety | Arm driver launched twice (I1). Any detection started the arm, no request needed (B6) | Duplicate removed behind a new static check. The arm starts only on a grasp request | T1.2, T1.25
Arm code | Unlocked reads, non-atomic state, a queue that grew without limit after each grasp (C2 to C4, C7) | Locks and atomic state. A second request now runs in simulation | T1.9, T1.14, T1.24
Nav | After any failed drive the goal bridge never sent another goal. All five nav nodes crashed on Ctrl+C (F1, F4, F5) | Failure paths answer, clean exit. Checked by the nav-node bench | T3.8
Voice | Word repeated many times per sentence. Arm's target word fixed as “box” in the source (B7, L1) | One word per finished sentence (31 messages to 3 on replay). Voice sets the arm's target | T2.10, T2.1
Wiring | 38 of 54 channel names scattered through the code | All 53 owned channels in config. 7-level bench and CI on every PR | T0.14

## Slide 47
GAPPLER · APPENDIX
BACKUP · A16
A16 Our memory graph vs HiCo-Nav's code
Answers: “Why not just run their code? What did you change?”
Source: ZONGZHE_PROGRESS_REPORT_2026-10.md §1.2, §2.2. hico-nav/PAPER_REPORT.md §4.8, §5.6. MEMORY_GRAPH_DESIGN.md D-MG1, D-MG2, D-MG6, D-MG12
48
Part | HiCo-Nav | Ours | Why
Where it runs | Habitat simulator (public code). A D455 depth camera on their robot | A recorded drive of our robot. Depth drawn from the LiDAR | We have LiDAR. No depth camera recording yet (T6.2)
Find objects | YOLO-World on every frame, MobileSAM on kept photos | SAM 3, all 30 classes in one pass | Already on our box (D-MG6). 5.7× faster batched
When to keep a photo | A detection, or the camera moved | The camera moved 1 m or turned 45° | No extra model on the shared GPU (D-MG12, tentative)
Language model | Qwen3-Omni API, or Qwen3-VL-8B offline | Qwen2.5-1.5B, local, text only | Theirs do not fit our 16 GB card
Match radius | 2.5 cm, hard-coded | 10 cm, in config | Two views of one object land 4 to 9 cm apart (A19)
Photos kept per object | 1 in the code | 3 | Keeps more than one viewpoint (D-MG1, tentative)
ALSO FIXED OR AVOIDED, FROM READING THEIR CODE
• Each graph link stored twice, synced by hand → stored once, with a consistency check
• No time limit on the language model → 10 s, then a CLIP fall-back
• Class ids from a Python set, can change between runs → an append-only list
• Task score on objects never set → set on insert, merge and new task
• Sort that depends on input order → sorted once by confidence, tested shuffled
• Fixed 20 px crop around each object → padding relative to the box
Their repo has no licence file, so the code was read, never copied.

## Slide 48
GAPPLER · APPENDIX
BACKUP · A17
A17 The photo gate: 29 photos, and what it costs
Answers: “What do you lose by keeping so few photos? Why 26 photos in one place and 29 in another?”
Source: bench-runs/2026-10-22-labbox-t6.5-pose-gate-sweep.txt. bench-runs/2026-10-21-labbox-t6.4-drive-run.txt (correction of 2026-10-22). D-MG12, T6.10
49
GATE SETTINGS ON THE LAB DRIVE (3,536 FRAMES, 1.85 S PER SAM 3 CALL)
Moved (m), turned (°) | Photos kept | Per minute | SAM 3 time | Saved vs every frame
0.5, 30 | 52 | 26.5 | 96 s | 98.5 %
0.5, 45 | 45 | 22.9 | 83 s | 98.7 %
1.0, 45 (used) | 29 | 14.8 | 54 s | 99.2 %
1.0, 90 | 22 | 11.2 | 41 s | 99.4 %
2.0, 45 | 24 | 12.2 | 44 s | 99.3 %
2.0, 90 | 14 | 7.1 | 26 s | 99.6 %
Every frame through SAM 3 would take 6,542 s. HiCo-Nav reports 30 to 60 photos a minute [paper]. We keep 14.8.
WHAT IT COSTS
A target coming into view does not add a photo by itself. HiCo-Nav runs a cheap detector (YOLO-World) on every frame for that. We chose the pose check alone for now: no new model, no GPU time on the shared card. Revisit after the talk (T6.10).
PHOTOS KEPT
29 of 3,536
54 s of SAM 3 instead of 6,542 s
26 OR 29?
29: the 1 m / 45° rule run over every frame.
26: the same rule applied to the 103 photos saved at a finer gate (0.25 m / 15°). The merge tuning (A19) used those 26. The conclusions hold at both 26 and 103 photos.

## Slide 49
GAPPLER · APPENDIX
BACKUP · A18
A18 LiDAR depth and the occlusion filter
Answers: “How sparse is the LiDAR? What does the filter do, and what does it cost?”
Source: ZONGZHE_PROGRESS_REPORT_2026-10.md §3.1, §3.4. MEMORY_GRAPH_DESIGN.md D-MG11. memory_graph/geometry.py drop_occluded, replay_loader.py
50
Frame 700, before the filter. LiDAR points coloured by distance:
farther points show between the chair's own.
PIXELS WITH A DEPTH READING
LiDAR scans used | Pixels
0.2 s | 1.6 to 2.4 %
1 s | about 7 %
1 s either side (used) | 12.8 to 14.4 %
THE RULE
Clear a pixel if any pixel in its 7 × 7 block is more than 10 % nearer.
ON A DEPTH CAMERA
Not needed. A D455 depth image is dense and already shows only the nearest surface.
FRAME 700, THE CHAIR
1.08 to 2.08 m
depth readings inside its outline
z −0.02 → 0.58 m
its centre: a floor patch, then seat height
7 cm
from the same chair seen in frame 2200, so they merge
WHAT IT COSTS
• Coverage 13.8 → 12.3 % on frame 700
• Something thin on a surface (paper on a wall) is within 10 % and keeps its background
• A few true far pixels at a near object's edge are cleared

## Slide 50
GAPPLER · APPENDIX
BACKUP · A19
A19 The answer key and the match radius sweep
Answers: “How do you know 8 to 3 is real? What is a false merge?”
Source: ZONGZHE_PROGRESS_REPORT_2026-10.md §3.5. bench-runs/2026-10-21-labbox-t6.4-drive-run.txt. MEMORY_GRAPH_DESIGN.md D-MG2. memory_graph/eval/, score_drive.py
51
Top-down LiDAR map, drive 1. Red: objects marked by hand.
First 12 shown, 16 in the final key.
Marked from the map and photos only. No SAM 3 or merge code used.
DUPLICATES / FALSE MERGES / MISSES, OUT OF 16 REAL OBJECTS
Match radius | Drive 1 (26 photos) | Drive 2 (14 photos)
1 cm | 31 / 1 / 3 | not run
2.5 cm (HiCo-Nav) | 8 / 0 / 4 | 2 / 0 / 7
5 cm | 4 / 0 / 3 | not run
7.5 cm | 4 / 0 / 3 | not run
10 cm (used) | 3 / 0 / 3 | 1 / 0 / 8
15 cm | 3 / 0 / 3 | 1 / 0 / 8, but a chair merged into its desk*
20 cm | 2 / 0 / 3 | not run
Merge by look only (2.5 cm) | 0 / 0 / 12 | not run
* Found by looking: the false-merge count misses some over-merging. Drive 2 lined up with drive 1 by ICP.
DUPLICATE
An extra graph object of the same kind on one real object
FALSE MERGE
Two real objects stored as one graph object
MISS
A real object with no graph object on it

## Slide 51
GAPPLER · APPENDIX
BACKUP · A20
A20 How the memory graph is tested
Answers: “Did you test it? What do the tests check?”
Source: memory_graph/tests/ (23 files, 399 tests). bench-runs/2026-10-23-labbox-t6.7-step5-tests.txt. ZONGZHE_PROGRESS_REPORT_2026-10.md §3.9
52
Stage | Tests | Example checks (test names, shortened)
Read the recording | 49 | Same wall from two poses lands in the same place. A wrong pose or depth scale misses by 20 cm or more
Keep a photo | 10 | A straight drive keeps a photo past every metre. Turning on the spot keeps one past every 45°
Find objects, masks | 86 | Detections sort the same when the input is shuffled. Batched SAM 3 gives the one-call answer
CLIP feature | 19 | Same chair scores above chair against other objects. Text and image vectors share one space
Merge sightings | 46 | Same chair from views 30° apart matches. Two identical chairs side by side do not merge
Keep photos, clean up | 53 | Every object keeps enough photos. A second pass does not grow the photo count
Ask the graph | 111 | A related object never outranks a target. A rejected object is skipped next time
Whole photo and drive | 25 | Three stored lab photos replayed through every stage still give the same objects
Grouped by test file. Stored lab photos with SAM 3's real output let most tests run without a GPU.
ON THE LAB BOX GPU
399 pass
None skipped, 23 Oct 2026. Real SAM 3, CLIP and Qwen models
CODE QUIZZES
After each task. The M6 quiz found 11 code issues: 3 correctness fixes landed (T6.9). The T6.7 quiz found 6, all fixed.
NOT SHOWN YET
The whole query on the full recorded drive, against the answer key (T6.8).

## Slide 52
GAPPLER · APPENDIX
BACKUP · A21
A21 From a sentence to classes: the reasoning check
Answers: “What if the model hangs? Why a small local model? What does “find a chair” really give?”
Source: bench-runs/2026-10-23-labbox-t6.7-reasoning-check.txt, local/t6.7/out/check_reasoning.json, 2026-10-23-labbox-t6.7-step5-tests.txt. memory_graph/config.py
53
22 INSTRUCTIONS, FROZEN BEFORE THE RUN
Model | Right, scored by script | Right, by hand | Reply time
Qwen2.5-1.5B (used) | 19 of 22 | 20 of 22 | 0.28 to 0.32 s
Qwen2.5-0.5B | 12 of 22 | not marked | 0.11 to 0.35 s
CLIP fall-back alone | 15 of 22 | 13 of 22 | 
FAILURES BY KIND (SCRIPT SCORE)
 | In list (5) | Synonym (4) | Attribute (3) | Indirect (4) | Relation (2) | Not in list (4)
1.5B | 0 | 2 | 0 | 0 | 0 | 1
0.5B | 0 | 4 | 3 | 2 | 0 | 1
Fall-back | 0 | 1 | 0 | 2 | 0 | 4
The slide's 20 of 22 is the hand score. Its 15 (fall-back) and 12 (0.5B) are script scores.
REAL REPLIES TO “FIND A CHAIR”
1.5B: chair. No related classes
0.5B: chair + cabinet, desk, shelf
Fall-back: chair
1.5B named related classes for 1 of 22. The prompt now asks for 2 to 5. Not re-run since.
SAFETY RULES
• Over 10 s, or an empty or unusable reply: CLIP picks the closest class
• Targets always rank before related objects
• Local: no API key, no network, nothing leaves the lab
• The paper's Qwen3-Omni needs 20 to 24 GB run locally [paper]

## Slide 53
GAPPLER · APPENDIX
BACKUP · A22
A22 Why a 24 GB card would help
Answers: “Why would 24 GB help? Why not run the paper's model?”
Source: ZONGZHE_PROGRESS_REPORT_2026-10.md §3.3 (measured peaks). hico-nav/PAPER_REPORT.md §6.4 (8B estimate, [inferred]). COMBINED_PROGRESS_REPORT_2026-10.md §9.3 item 5
54
GPU MEMORY, GIB
0
8
16
24
Our card (RTX 4060 Ti)
16
A 24 GB card
24
SAM 3 + 8B model
SAM 3 10.3
8B model, 8
+8 uncompressed
SAM 3: measured peak, all phrases batched 16 per pass. 8B model: estimate, 8 to 16 GB depending on compression.
READING IT
SAM 3 plus a compressed 8B model (up to about 13 GB) fits in 24 GB, never in 16. Uncompressed (16 GB) it does not fit in 24 either.
ALSO ON THE SAME CARD
• The SAM 3 service
• AnyGrasp
• CLIP
• Whisper (speech)
• Two Qwen models
Shared by 3 people and the CI runner. They have never all run together: each part is tested alone.

## Slide 54
GAPPLER · APPENDIX
BACKUP · A23
A23 The reclarification node (planned)
Answers: “What is the reclarification node? How does it talk to the user?”
Source: task-tree.html T11.4, T11.7, T11.8. PROJECT_PLAN.md §5.1 (M11). Not started: about 10 hours, M11 forecast 21 Dec 2026 to 21 Feb 2027
55
Orchestrator
Request unclear, e.g. two identical boxes
USER_CLARIFICATION_NODE · AN LLM LOOP (T11.8)
Search the graph
by text
List candidates
Describe one
position, nearby objects
Ask the user
one question
The model picks a tool each turn, until it can end. At most 3 questions for now.
Phone web page (T11.7)
Speaks the question with the phone's own voice, can show pictures of the candidates. No app. The glasses have no speaker
IT ENDS WITH ONE OF
CHOSEN
one graph object id
LEAD
where to look next, sent to exploration
NEW_REQUEST
the user asked for something else
USER_GAVE_UP
IT NEVER MOVES
Only the orchestrator acts on its answer. It is the only node that starts motion (T11.4).