## Slide 1
[INSERT PHOTO: full robot with the Aria glasses beside it]
RealMan RM65 arm on the Hexman ECHO-PLUS base, Livox LiDAR and front D455 visible. Half-bleed, crop to fill
Owner: any member, take at the lab
High-Readiness Mobile Manipulation via Gaze-Speech Interaction and Continuous Pre-Alignment
Look at it, name it, and the robot fetches that one
Dion, Sherman, Zongzhe
Supervisors: Prof Yuan Shenghai, Prof Xie Lihua
Interim assessment, 28 October 2026
Notes: PRESENTER: Dion SLOT: 0:20 ELAPSED AT END OF SLIDE: 0:20 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) Good afternoon. We are Dion, Sherman and Zongzhe. Our project is a mobile robot that fetches the specific object a person looked at and named, even when the robot cannot see that object at the start. TRANSITION Here is the situation we want the robot to handle. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [ARTEFACT NEEDED: one photo of the full robot with the glasses beside it (any member, take at the lab)] Note: the approved title says "Continuous Pre-Alignment", a term the report never uses. Keep the title. Dion explains it if asked in Q&A.

## Slide 2: The user can see the object. The robot sees neither the user nor the object
User's glasses
1 to 3 m away, front on
[INSERT BASE-CAMERA FRAME FROM KNEE HEIGHT]
Ideally the same box seen by the D455. Else a frame from mg_handdriven1_survey_every_100th_frame_2026-10-21.jpg or nav_camera_frames_along_t35f_run1_2026-10-21.jpg, captioned "the lab from the base camera"
Owner: Sherman or Zongzhe
Robot base camera
knee height
Robot wrist camera
0.2 to 0.5 m, from above
Same object, three viewpoints, almost nothing in common pixel for pixel
Why it matters: assistive use, where a user can look but cannot easily point or speak, in a scene full of similar mugs, pill bottles and cans
Glasses and wrist crops: clip_glasses_vs_wrist_crops_2026-10-20.jpg (T8.7 pairs)
Dion
Notes: PRESENTER: Dion SLOT: 0:50 ELAPSED AT END OF SLIDE: 1:10 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) Picture a user wearing Meta's Aria glasses. They look at a box on a table and say 'pick up that box'. The robot is somewhere else in the room. It has never seen the user's view. These three images show why that is hard. On the left is what the glasses see: the box from a metre or two away, front on. In the middle, the robot's base camera, at knee height. On the right, the wrist camera on the arm, looking down from twenty centimetres. Same object, but the images have almost nothing in common. Yet the robot has to find, and pick up, exactly the box the user looked at. TRANSITION Two published systems each solve half of this. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [ARTEFACT NEEDED: a base-camera frame from knee height. The memory graph answer key has no box, so a frame of the box may not exist. Use a frame from Zongzhe's mg_handdriven1_survey_every_100th_frame_2026-10-21.jpg or Sherman's nav_camera_frames_along_t35f_run1_2026-10-21.jpg, captioned "the lab from the base camera", or take one frame of the box with the D455 at the lab (Sherman or Zongzhe)]

## Slide 3: Objective: join FAM-HRI's gaze and speech with HiCo-Nav's exploration and memory
Main objective: a mobile manipulator that takes a spoken command and the user’s gaze, explores a room it cannot see at the start, finds the object the user looked at, drives to it and grasps it
FAM-HRI Lai et al., 2025
What it does
Meta Aria glasses: gaze and speech tell a robot arm which object to pick
What we take
Speech to an object word, gaze to pick the object, the arm grasp
What it cannot do for us
The object must already be in front of the arm
HiCo-Nav Xu et al., ICRA 2026
What it does
A robot explores an unseen room, builds a memory graph of every object it sees, and answers language queries
What we take
3D pose from FAST-LIVO2, the memory graph (3D position and CLIP image feature per object), sentence to object classes, exploration
Not taken: its own motion planner (we send goals to Nav2). Its smarter exploration order is optional (M9)
What it cannot do for us
It finds a class ("a box"), not the one you mean
What we add to join them: the robot compares each object it finds with the object the user looked at, drives to the match, and confirms it with the wrist camera before grasping
Evaluation: end-to-end trials, success counted per phase
Dion
Notes: PRESENTER: Dion SLOT: 1:20 ELAPSED AT END OF SLIDE: 2:30 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) Our objective is a mobile manipulator that takes what the user says and where they look, explores a room it cannot see at the start, finds that object, drives to it and grasps it. Two published systems each solve half of this. FAM-HRI uses the same Aria glasses: speech gives the object word, gaze picks which object, and an arm grasps it. But it assumes the object is already in front of the arm. We take its user side: speech, gaze and the grasp. HiCo-Nav is a robot that explores an unseen room and builds a memory graph of every object it sees, each with a 3D position and an image feature. But you query it with a sentence, so it finds a class, any box, not the one you looked at. We take its pose estimation, its memory graph, its sentence reasoning and its exploration. We leave out its own motion planner and send goals to Nav2 instead. Its smarter way of choosing where to explore next is optional. What we add is the join. The robot compares each object it finds with the one the user looked at, drives to the match, and checks it with the wrist camera before grasping. TRANSITION Here is the full behaviour we are building towards. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [VERIFY: FAM-HRI's full title and author list (D§1.1 flags it unverified), in case it goes on the slide]

## Slide 4: The target system works in five phases
1 Intent capture
Speech gives the word, gaze picks the object, crop it
Tested on replay
Dion
2 Explore and find the user
Explores, maps the room and remembers objects with 3D position and image feature. Looks for the user first
Map tested live (pushed by hand)
Memory graph tested offline
Exploration and finding the user planned
Sherman, Zongzhe, Dion
3 Search
Compare each object with the gaze target. A match ends exploration
Graph search built for sentences
Gaze match planned (T8.2)
Zongzhe, Dion
4 Approach and confirm
Drive to the object. The wrist camera confirms it is the same one
Confirm tested on replay, now steers the grasp
Driving planned
Dion, Sherman
5 Grasp
Grasp candidates on the wrist point cloud, plan, execute
Tested on the real arm
Dion
Tested
Built, not validated
Isolated (works alone)
Planned
Owner under each phase
Scope decisions
Exploration is the core of the search. The paper’s smarter exploration order (M9) is cut first if time runs short
Finding the user speeds up exploration: the object is somewhere the user can see
Out of scope: bringing the object back to the user
Final demonstration target: March 2027 (M10)
Zongzhe
Notes: PRESENTER: Zongzhe SLOT: 1:15 ELAPSED AT END OF SLIDE: 3:50 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) The finished system works in five phases. First, the user speaks and looks. Speech gives us the word, gaze tells us which object, and we cut an image crop of it and turn it into a CLIP feature. Second, the robot explores. It maps the room and builds a memory of the objects it sees, each with a 3D position and an image feature. It looks for the user first, because the object is somewhere the user can see. Third, it compares what it sees with the user's target. A good match tells it to stop exploring. Fourth, it drives close and the camera on the arm confirms that this is the object the user meant. If not, it goes back to exploring. Fifth, it grasps. Exploration is the core of the search. HiCo-Nav also has a smarter way to choose where to explore next. That part is optional and the first thing we cut if time runs short. Bringing the object back to the user is out of scope. The badges show where each phase stands seven weeks in. The next eleven minutes go through them in order. TRANSITION Before the results, a word on where we started and how we work.

## Slide 5: We inherited code that did not run, so we built a test bench and a contract first
September 2026 starting point
A year of code from an earlier team. No tests, no CI
One program moved the real arm within seconds of starting, unprompted
The AnyGrasp path was unreachable
Navigation ran only from another user’s private workspace, and the repo copy did not build
No memory graph code
Dion
Glasses, cross-camera matching, arm and grasp, test bench and CI
Builds on
Aria SDK, SAM 3, AnyGrasp, MoveIt 2
Leads
M1, M2, M4, M7, M8
Sherman
Mobile base, LiDAR, camera mount, mapping and localisation
Builds on
FAST-LIVO2, Nav2, SLAM Toolbox
Leads
M3, M5 (mount)
Zongzhe
Memory graph, sentence reasoning, navigation goal nodes
Builds on
HiCo-Nav method, open_clip, Qwen2.5
Leads
M0, M6, M9
Shared base: channel contract naming the owner of every topic and frame + 7-level test bench (L0 static checks to L6 real robot) + CI on every PR, plus a GPU runner on the lab machine
Baseline first, then replace: keypoint matching measured before CLIP replaced it
Hardware one step at a time: written pass rule, saved log, two people present
Sherman
Notes: PRESENTER: Sherman SLOT: 0:45 ELAPSED AT END OF SLIDE: 4:40 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) We did not start from a working system. The inherited code had no tests and no CI, and none of it ran from a fresh copy. One program homed the real arm within seconds, with no prompt. Navigation ran only from another user's workspace, and our copy did not build. There was no memory graph. So we built foundations first. Dion took the glasses and the arm, I took the base and mapping, and Zongzhe the memory graph. A channel contract says who owns every message and frame, and a seven-level test bench runs on every pull request. We measure a baseline before replacing anything, and on the real robot we move one step at a time, with two people present. TRANSITION Phase one: turning a sentence and a glance into a target.

## Slide 6: Speech gives the word, gaze picks the object
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
1 Voice
Speech detector, Whisper, small language model returns one object word ("box"). One message per sentence, down from 31
2 Pick the moment
The glasses frame from when you spoke (gaze window of 1.0 s)
3 Segment
SAM 3 finds every "box" in that frame
4 Gaze vote
Each gaze sample votes for the mask under it. Winner needs half the votes. Crop its box plus 20 px: the reference crop goes to the robot
1.0 m: gaze on the box, box picked
1.5 m: gaze landed on the mats
gaze landed on the mats
Blue ring: gaze. Box outline: masks SAM 3 found. Frames from aria_gaze_pick_vs_distance_2026-10-20.jpg
60 of 61
frames, right box
recording, 1.4 to 2.4 m, steady stare
4 of 4
spoken words produced a reference crop
full chain on replay
Word ready about 1.1 s after speech ends
Limit: gaze is off by about 5.6 degrees (60 px at 1.4 m), about 15 cm at 1.5 m. At 1.5 m it landed on a stack of mats
Tested
on recordings and replay. Live glasses stream still throttled on the lab machine
Dion
Notes: PRESENTER: Dion SLOT: 1:20 ELAPSED AT END OF SLIDE: 6:05 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) The user says 'find the box'. A speech detector waits for the sentence to finish, Whisper turns it into text, and a small language model pulls out the object word. Before this, the old pipeline produced thirty-one messages per phrase. Now it produces one. Gaze runs at the same time. We keep the last twenty seconds of glasses images and gaze points, so we can go back to the moment the user was speaking. SAM 3, a segmentation model you prompt with a word, finds every box in that one frame. Then gaze votes. Each gaze sample in a one-second window votes for the mask it lands on, and the winner needs half the votes. We crop that mask with a small margin. That crop is what we send to the robot. On a recording at 1.4 to 2.4 metres, this picked the right box in 60 of 61 frames. On a full replay, all four spoken words produced a crop. The limit is gaze accuracy. The eye model is off by about five and a half degrees, roughly 15 centimetres at 1.5 metres. Here, at 1.5 metres, it landed on a stack of mats that SAM 3 also called a box. Keep that case in mind. It comes back on slide 12. TRANSITION That crop now has to be found by a robot that has never seen this view. Sherman will show how the robot knows where it is. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [ARTEFACT NEEDED: aria_gaze_pick_vs_distance_2026-10-20.jpg from docs/dion_docs/local/report_media/ (Dion)] [VERIFY: whether T2.21 (word timestamps from Whisper, PR #91) has merged by 28 Oct. If yes, the script can say the word is stamped with the time it was spoken. If not, keep as is]

## Slide 7: The base builds a coloured 3D map that closes within 12 mm over a 26 m loop
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
[INSERT MAP BUILD-UP ANIMATION]
nav_fastlivo_map_buildup_clean_handdriven1_2026-10-24.gif (10 s, about 12x). Alt: ..._map_orbit_clean_... .gif. Still fallback: ..._map_iso_clean_... .png. Orange line = path, green dot = start, white square = end
Owner: Sherman
[INSERT CLOSURE ZOOM]
nav_fastlivo_path_closure_zoom_clean_handdriven1_2026-10-24.png
Owner: Sherman
10 cm zoom, bar = 2 cm, start to end 12 mm
What it is: FAST-LIVO2 fuses the Livox MID-360 LiDAR, its IMU and the base D455 colour camera into a pose and a coloured map. The HiCo-Nav paper uses it for its camera poses, with the same LiDAR
Why 3D, not 2D SLAM: the memory graph places every object in 3D from the camera pose, so it also needs height, pitch and roll (1 degree of pitch moves an object 4 m away by about 7 cm). Nav2 still drives on a 2D grid, fed by this pose
2D
x, y, heading
3D
full pose
Hand-pushed loop, recording handdriven1, 20 Oct
12 mm
26.05 m loop, back to start within 12 mm
4 mm LiDAR-only, 7 mm odometry error, 0.03 %
6.7 cm
mid-route error at most
at the floor of our reference (about 7 cm)
11 to 14 ms
per frame on the CPU
inside the 100 ms scan period
Limit: pushed by hand, not driven. Nav2 has never driven the base
ROS 1 to ROS 2 port
15 to 22 Oct
1 Build
sealed container
2 Authors’ data
14,850 / 14,850
3 Our sensors
every message audited
4 Silent defects
3 found, fixed
5 Live
26 m loop
6 Hand to Nav2
tilt under 0.5 deg
Sherman
Notes: PRESENTER: Sherman SLOT: 1:35 ELAPSED AT END OF SLIDE: 7:45 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) Before the robot can remember where objects are, it needs to know where it is. We use FAST-LIVO2, the method the HiCo-Nav paper uses, from the University of Hong Kong. It fuses the LiDAR, its motion sensor and the colour camera into one pose, and paints a coloured 3D map. Why 3D? 2D SLAM knows only where the base is on the floor and which way it faces. The memory graph places each object in 3D from the camera's pose, so an unmeasured tilt moves objects by centimetres. Nav2 still drives on a 2D grid built from this pose. FAST-LIVO2 is published for ROS 1. We run a community ROS 2 port, and getting it to work was most of the effort. The strip along the bottom shows the steps. I proved it on the authors' own recording first, then on our sensors with every message checked. I found three defects that fail silently: no crash, just a wrong map. Each was found by reading the source and confirmed against a control run. The result: I pushed the base by hand around a 26-metre loop. The path returns to its start within 12 millimetres, and the mid-route error is within about 7 centimetres, the limit of our reference. The pose now feeds Nav2's frame tree. Nav2 driving the base is the next test. TRANSITION A map is only useful to the arm and the memory if every camera's position on the robot is known. That is a calibration question, and there are several of them. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [VERIFY: the clean renders are in Sherman's gitignored docs/sherman_docs/local/report_media/, so the links above work on his machine only. Sherman copies them to whoever builds the slides] [VERIFY: the venue can play video. Fall back to the GIF or the iso still]

## Slide 8: Four camera relationships, four different states of calibration
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
frames also serve phases 4 and 5
[INSERT LIDAR-ON-CAMERA OVERLAY]
nav_lidar_on_camera_overlay_stationary02_t0s_2026-10-19.png
Owner: Sherman
before calibration: LiDAR points over the camera image
Base
D455
LiDAR
Arm
Wrist D435i
User + Aria glasses
1
2
3
4
Schematic side view, not to scale
1
Base to arm
Measured
Used for: Arm grasps in the base’s map
(0.18, 0, 0.48) m, yaw 180 degrees, matched on the robot. Base origin (floor, under the drive axle) checked against the vendor manual
2
Base camera to LiDAR
Mount measured, not calibrated
Used for: Object positions and depth in the memory graph
Measured to the camera’s mounting hole, Intel’s published dimensions from there. Rotation set by construction (flush on vertical aluminium extrusions), not measured with a tool. Mount values wired and unit-tested (12 software checks). Not yet calibrated to the LiDAR: about 6.7 px of error per degree. Rig planned (T5.5)
3
Wrist camera to arm
Calibrated
Used for: Turning a grasp seen by the camera into an arm goal
4
Glasses to robot
Planned (T8.8)
Used for: A gaze ray in the robot’s own 3D frame, for look-alike objects
Three methods ranked
Line key: green, measured or calibrated. Amber, measured, not calibrated. Grey dashed, planned
Camera calibration (where is one camera relative to another) is a separate problem from the robot’s frame tree (where each part is relative to the base)
Sherman
Notes: PRESENTER: Sherman SLOT: 1:10 ELAPSED AT END OF SLIDE: 8:55 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) There are four places where we need to know how one part of the robot sits relative to another. The arm on the base is measured. We set the transform from the mount drawings and checked it on the robot. The base's own origin, on the floor under the drive axle, matches the vendor's manual. The base camera relative to the LiDAR is measured but not calibrated. I designed and fitted the mount, measured to the camera's mounting hole, and took the rest from Intel's published camera dimensions. It sits flush on vertical aluminium extrusions, so it points straight by construction. What is left is a calibration against the LiDAR itself, because one degree of error moves a point by about seven pixels. The rig for that is planned. The wrist camera relative to the arm is calibrated, so a grasp it sees becomes an arm goal. The last one is different in kind. To use gaze to separate two identical objects, the robot needs the user's gaze ray in its own frame, which means locating the glasses relative to the robot. That is planned for January. None of these blocks today's results, but each one blocks a specific later step. TRANSITION With poses and camera images from that drive, Zongzhe builds the robot's memory of the room. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [ARTEFACT NEEDED: nav_lidar_on_camera_overlay_stationary02_t0s_2026-10-19.png (Sherman)] [VERIFY: optional before the talk, a phone inclinometer on the camera top would turn "straight by construction" into a measured pitch and roll (Sherman)] [TEAM INPUT REQUIRED: one phrase on how the wrist camera was calibrated (method, residual), in case an examiner asks. Dion confirmed on 2026-10-24 that it is calibrated] [VERIFY: who presents the glasses-to-robot row. It is Dion's task (T8.8). Sherman can present it as written, or Dion can add one sentence in his later block]

## Slide 9: The memory graph turns a drive into objects with a position and an image feature
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
Objects: merged 3D points, a box, an averaged CLIP image feature, a class label
Anchors: kept photos with the camera pose, linked to the objects they show
How it is built, in 14 tested stages
Keep a photo every 1 m or 45 deg
SAM 3 finds all 30 classes
LiDAR gives depth
Lift to 3D
CLIP feature per object
Merge repeat sightings
[INSERT RERUN 3D VIEW OF THE GRAPH]
Grey LiDAR room, each object a labelled box, each anchor a small camera at its pose, lines from cameras to the objects they saw. Screenshot from mg_t6.3_four_photos_rerun_3d_2026-10-21.rrd, or the flythrough video
Owner: Zongzhe
[INSERT FRAME 700: PHOTO | SAM 3 MASKS | 3D BOXES]
mg_frame700_masks_and_3d_objects_2026-10-21.png
Owner: Zongzhe
Isolated
Built offline from a recorded drive. Not yet built live while driving
Recording handdriven1, 3536 frames
29 photos kept
99.2 % of segmentation time saved
1.69 s vs 9.70 s
batched SAM 3: 40 phrases, 5.7 times faster than one at a time
399 tests pass
on the lab GPU
9 upstream problems
fixed or avoided, for example the language model call had no timeout, and the task score was never set
Zongzhe
Notes: PRESENTER: Zongzhe SLOT: 1:20 ELAPSED AT END OF SLIDE: 10:20 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) The memory graph is HiCo-Nav's idea. As the robot moves, it keeps a photo now and then, finds the objects in it, and stores each object with its position in 3D and a CLIP image feature. CLIP is a model that turns an image into a vector, so that similar-looking things get similar vectors. The photos are kept too, linked to the objects they show. That link is the 'graph'. HiCo-Nav published code, but with no licence, so I read it and wrote a fresh implementation as fourteen separate stages, each with its own tests. Reading it also turned up nine problems, such as a language-model call with no timeout, which we fixed or avoided. Here is the graph built from Sherman's hand-pushed drive. Two choices keep it fast. A photo is kept only after the robot moves a metre or turns 45 degrees, so 29 of 3,536 frames go to segmentation, which saves over 99 % of that time. And all thirty object classes go through SAM 3 in one batch, 5.7 times faster than one at a time. It is built offline from a recording. Building it live while the robot explores is next (T7.2, T7.5). TRANSITION The hardest part of building it is deciding when two sightings are the same object. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [ARTEFACT NEEDED: Rerun 3D screenshot or mg_graph_3d_flythrough video (video is a stub, recordable any time from the .rrd), and mg_frame700_masks_and_3d_objects_2026-10-21.png, from docs/zongzhe_docs/local/report_media/ (Zongzhe)]

## Slide 10: A 10 cm merge radius cut duplicates from 8 to 3 with no false merges
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
Chart: Match radius (cm)
| 1 | 2.5 | 5 | 7.5 | 10 | 15 | 20 | 2.5 | 6 | 10 | 12 | 15
Duplicates, drive 1 | 31 | 8 | 4 | 4 | 3 | 3 | 2
False merges, drive 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Duplicates, drive 2 (run at 2.5, 10, 15 cm only) | 2 | 1 | 1
Duplicates, drive 1
False merges, drive 1
Duplicates, drive 2 (run at 2.5, 10, 15 cm only)
chosen: 10 cm
drive 1: 8 at 2.5 cm, 3 at 10 cm
15 cm: chair merges into desk (drive 2)
Why not appearance: CLIP similarity
Same chair
0.934
Two chairs, same model
0.81 to 0.85
Other objects
0.56
Method
A hand-made answer key of 16 real objects marked on the LiDAR map (7 chairs, 2 tables, 2 TVs, 2 computer towers, shelf, sofa, door). Independent of the code under test
Why the radius
Two views of one object land 4 to 9 cm apart with sparse LiDAR depth. Upstream’s 2.5 cm was too tight
Result at 10 cm: duplicates 8 to 3, 0 false merges, misses unchanged at 3 (first drive). Second drive: 2 to 1
Trade-off
At 15 cm a chair merges into its desk on the second drive, so 10 cm, not 15
Appearance alone
Two chairs of the same model score 0.81 to 0.85. Merging on appearance alone removes duplicates by merging everything (10 to 14 of 16 objects missed)
Two drives, 16 objects. A difference of one is noise
Zongzhe
Notes: PRESENTER: Zongzhe SLOT: 1:00 ELAPSED AT END OF SLIDE: 11:20 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) The robot sees the same chair from many places. Each sighting must merge into one object, and two chairs side by side must stay two. To measure that, I made an answer key by hand: sixteen real objects marked on the LiDAR map, without using any of the code being tested. Then I swept the settings. The lever is the match radius, how close two sightings' points must be. With our sparse LiDAR depth, two views of one object land 4 to 9 centimetres apart, so upstream's 2.5 centimetres split objects. At 10 centimetres duplicates fall from 8 to 3 with no false merges. On a second drive, 2 to 1. At 15, a chair merges into the desk next to it, so we chose 10. Why not just merge things that look alike? Because look-alikes are exactly the problem. CLIP scores two chairs of the same model at 0.81 to 0.85, close to the same chair at 0.93. Merging on appearance removes every duplicate by merging nearly everything. That is also why the class alone cannot find the user's object. TRANSITION Once the objects are in the graph, the robot has to find the right one from a sentence. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [ARTEFACT NEEDED: the line chart, built from the table above (slide session can draw it), optional mg_ground_truth_12_objects_on_lidar_map_2026-10-21.png (Zongzhe)]

## Slide 11: A sentence becomes a ranked list of objects with 3D positions
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
1 Sentence to classes
2 Score
3 Rank
"Find the chair"
A local language model (Qwen2.5, 1.5B) returns target and related classes
target: chair
related: table, desk
Each object’s CLIP image feature against the sentence’s CLIP text vector
object image feature
vs
sentence text vector
Target classes first, then related, each by score
Each hit: object id, 3D centre, best photo
A wrong hit can be rejected and skipped next time
Acceptance run pending (T6.8)
Sentence to classes, 22 test instructions (checked by hand)
Qwen2.5 1.5B (used)
20 of 22
Fallback without the model
15 of 22
Smaller 0.5B model
12 of 22
0.28 to 0.32 s
a reply, running locally
Built
Steps 2 and 3 tested on stand-ins and a few photos. The full query on the recorded drive is the acceptance test, scheduled weeks 7 to 8 (T6.8)
Today the query is a sentence. In the full system each object is matched against the gaze crop’s feature, and a match ends exploration (M8)
Zongzhe
Notes: PRESENTER: Zongzhe SLOT: 0:50 ELAPSED AT END OF SLIDE: 12:10 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) To search the graph, the robot first turns the sentence into classes. A small language model, running locally, returns the target class and some related ones. 'Find the chair' gives chair, plus table and desk, because chairs are usually near them. The 1.5 billion parameter model got 20 of 22 test instructions right and answers in about a third of a second. Then every object is scored by comparing its stored image feature with the sentence, using CLIP again. Target classes rank first, related ones after. Each hit comes with a 3D position and the best photo of it, and a wrong hit can be rejected so the robot tries the next one. The ranking has been tested on stand-in data and a few photos. Running the full query on the recorded drive, checked against the answer key, is the next milestone, in the next two weeks. Today the query is a sentence. In the full system, the robot matches each object against the gaze crop from slide 6, and a good match tells it to stop exploring and go to the user's chair, not just any chair. Dion now picks up the object at close range. TRANSITION (Handover) "Thanks, Zongzhe. When the robot reaches the object, it has to confirm, with the camera on its wrist, that this is the one the user looked at. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [VERIFY: the "related: table, desk" example. Zongzhe to replace it with the model's actual output for "find the chair" from check_reasoning.json] [ARTEFACT NEEDED: the 22-instruction right/wrong grid from local/t6.7/out/check_reasoning.json (Zongzhe)] [AFTER T6.8: if the acceptance run happens before 28 Oct, replace the status line with its result]

## Slide 12: CLIP finds the looked-at box across cameras, and now steers the grasp
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
The question: which wrist-camera mask is the object in the glasses crop?
1 Choose the method
25 glasses-wrist pairs with 2 to 12 decoys, unless noted. Share of pairs with the box ranked first
SuperPoint + LightGlue keypoints (baseline, 15 pairs)
0 of 15
SAM 3 decoder vector
7 of 25
SAM 3 image features
15 of 25
CLIP whole-object feature
25 of 25
Baseline: keypoints match the ceiling and floor, not the box
2 In the grasp loop (T8.9a)
The grasp client compares every wrist mask with the glasses crop and takes the closest. Below 0.56, or a tie within 0.01, it publishes nothing and the arm waits
glasses above, wrist below
Wrist targets on the box the user looked at (recordings replayed, arm not moved)
Three different boxes
Old pick (most confident SAM 3 mask)
91 % 105 of 115
With the glasses crop
100 % 334 of 334
Two cardboard boxes, 0.4 to 1.6 m
Old pick (most confident SAM 3 mask)
0 % 0 of 114
With the glasses crop
99 % 266 of 268
Replayed recordings, counted per published target. Not yet run on the real arm
The 2 misses: wrong gaze pick at 1.5 m (the mat). Fix next: T2.24
Limit: same-colour boxes 6 of 12. Needs the gaze ray in the robot frame (T8.8)
Dion
Notes: PRESENTER: Dion SLOT: 1:35 ELAPSED AT END OF SLIDE: 13:50 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) This is the central perception problem. We have the glasses crop from slide 6, and the wrist camera sees several objects. Which one is it? The obvious approach is keypoint matching: find distinctive points in both images and pair them. We measured that first. It ranked the box first in none of 15 pairs. The viewpoints differ too much. So we compared whole-object features, and CLIP ranked the right box first in all 25. This week we put it where it matters, inside the grasp client. The arm now goes for the box you looked at, not the box SAM 3 is most confident about. On a scene with two cardboard boxes, the old pick took the wrong box in all 114 frames. With the glasses crop, 266 of 268 targets were the right box. With three boxes, 334 of 334. If nothing matches well enough, the arm waits. The two misses are instructive. They came at 1.5 metres, where gaze landed on the mat. The crop was wrong before the matcher ever saw it. So the next step is to refuse weak gaze picks at the glasses. The real limit is identical objects: two boxes of the same colour, 6 of 12. Appearance cannot separate them. That needs the gaze ray in the robot's frame, the glasses calibration from slide 8. All of this is on replayed recordings. The real arm run comes next. TRANSITION Once the target mask is chosen, the arm has to pick it up. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [VERIFY: CR§8.2 also lists "two similar cardboard boxes 148 of 180" from T8.5 (matcher on display). The T8.9a cardboard scene gives 266 of 268. The counts differ in what they count (T8.9a counts only published targets, refusals excluded) and possibly in the recording. The slide uses only the T8.9a figure. Dion to confirm before anyone quotes both] [ARTEFACT NEEDED: lightglue_baseline_wrong_matches_2026-10-19.jpg and clip_glasses_vs_wrist_crops_2026-10-20.jpg (Dion). The two bar charts can be drawn from the tables above]

## Slide 13: The real arm grasps on a spoken command: 5 of 6 within reach
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
Idle
Approach
Grasp
Hold
grasp request + mask
wrist camera at 0.21 m
lift, return home
"release"
Stopped
stop key
reset, no motion
Approach: the wrist camera steps 2 cm towards the mask centre until 0.21 m
Hold: until the user says "release"
[INSERT VIDEO OF THE REAL GRASP]
grasp_real_arm_<date>.mp4 (Dion’s phone), trimmed to 15 s or less. Or three stills: approach, close, lift. Keep a still as backup if playback fails
Owner: Dion
Grasps by box distance
4 of 4
44.5 cm
1 of 2
49.5 cm
0 of 2
54.5 cm
reach limit
■ grasped ■ failed
Real RM65 arm, simple grasp path, command from a recorded voice file
5 of 6
within reach (5 of 8 grasps)
First real grasp 13 Oct 2026
Grasp, hold, refuse two requests while busy, release, grasp again, in one run
Software stop: arm stopped at two test points, motion cancelled within 1 ms
Conditions and limits: voice from a recorded file, not live glasses. Box in a narrow band of positions. Success judged by the people at the robot, no automatic check yet. Hardware e-stop is rejected by the arm controller, so every test has two people and a hand on the power button
Dion
Notes: PRESENTER: Dion SLOT: 1:10 ELAPSED AT END OF SLIDE: 15:00 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) Grasping is a state machine. The arm only accepts a target after a grasp request, and only when idle. It then steps the wrist camera towards the target mask, two centimetres at a time, re-checking at each step, until it is 21 centimetres away. This is a simple form of visual servoing: small corrections absorb calibration and depth errors. Then it grasps, lifts, returns home, and holds the object until the user says 'release'. Our first real grasp was on 13 October. Started from a recorded spoken command, the arm made 5 of 8 grasps. Both failures at 54.5 centimetres were out of reach, so within reach it was 5 of 6. Safety came first. The arm's hardware stop is rejected by its controller, so we wrote a software stop. On the real arm it cancels motion within a millisecond. Every motion test still has two people and a hand on the power button. These grasps used a simple grasping method, one blind step and close. Next we will look at the learned grasp model we used to propose more complicated grasps. TRANSITION The learned grasp model, AnyGrasp, is where the current blocker sits. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [ARTEFACT NEEDED: phone video of the real grasp, grasp_real_arm_<date>.mp4. Dion has it, not yet copied into local/report_media/ (Dion)] [VERIFY: whether any grasp has now run with the live glasses instead of a WAV file. If yes, update the conditions line]

## Slide 14: AnyGrasp works at one ideal spot because, up close, the camera sees only one face
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
AnyGrasp: a learned model that proposes 6-DoF grasps on a point cloud. Result: 2 of 3 at the ideal spot (44.5 cm, centred, square). Fails elsewhere: a recipe from OK-Robot gave more grasps offline (132 vs 97) but 0 of 4 live
A 75 mm face measured as 56 mm: the check passes a grasp the gripper cannot make
Gripper opening against each face
Side face 75 mm
gripper 71 mm
✗
too wide
Top 60 mm
gripper 71 mm
✓
fits
Box 75 x 60 x 143 mm
Cause, diagnosed
At 0.21 m the wrist camera sees mostly one face of the 75 x 60 x 143 mm box
The confident grasps go across the 75 mm face, wider than the 71 mm gripper
Our fit check measures width from visible points, so edge and corner grasps pass it wrongly (369 of 369 passed on replay)
The good top-down grasp is proposed in 49 of 75 frames but scores at most 0.25, under our 0.3 floor
Next, cheapest first
A Grasp once from 0.4 to 0.5 m with the whole box in view
B Grasp on several fused views (retest owed)
C New AnyGrasp SDK (waiting on a licence)
Dion
Notes: PRESENTER: Dion SLOT: 1:00 ELAPSED AT END OF SLIDE: 16:00 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) AnyGrasp is a learned model that looks at a point cloud and proposes grasps: where to put the gripper and at what angle. At the ideal spot it worked twice in three tries. Anywhere else it failed. We traced why. The arm runs AnyGrasp when the camera is 21 centimetres from the box, and from there it sees mostly one face. AnyGrasp's most confident grasps go across the 75-millimetre face, but our gripper opens to 71. Our own fit check should catch that, but it measures width from the points it can see, so a grasp on an edge looks narrow enough and passes. On replay every one of 369 grasps passed it. The grasp we want, from the top across 60 millimetres, is proposed in most frames, but scores 0.25, under our floor. So the problem is not the model. It is where we ask it. The cheapest fix is to run AnyGrasp once from further back, 40 to 50 centimetres, with the whole box in view, then make one planned move. The second is to fuse several views into one cloud, which is built and needs a retest. This decides when M1 closes. TRANSITION (Handover) "Sherman will now step back from the parts and show what is connected today. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [ARTEFACT NEEDED: fit_check_edge_grasp_75mm_face_measured_56mm_passes_wrongly.png, optional anygrasp_8_best_grasps_angles_2026-10-20.png (Dion)] [VERIFY: if the new SDK licence (T1.45) or the fusion retest (T1.47) has a result before 28 Oct, add one line. Otherwise keep as is]

## Slide 15: Where each part sits in the full flow, and the links still to join
1 Intent capture
2 Explore and find the user
3 Search
4 Approach and confirm
5 Grasp
Voice and gaze to a reference crop
Tested on replay
FAST-LIVO2 map and pose
Tested, pushed by hand
Nav2 drives the base
Built, never driven
Memory graph
Works alone, offline
Find the user
Planned
Gaze match against graph objects
Planned
Drive to the object, hand over to the arm
Planned
Wrist camera confirms the object
Tested on replay
Grasp on the real arm
Tested on the real arm
1 recorded voice word (real arm)
2 gaze reference crop (replay)
3 target mask, 600 of 602
4 pose and 2D map, checked live
5 recorded drive, offline
6 explore, graph grows live (T3.6, T7.5, T7.2)
7 find the user (T7.6)
8 gaze target (T8.2)
9 each new object (T8.2)
10 match becomes the goal (T7.1, T6.8)
11 arrive, hand over (T3.7)
12 reject: explore again (no task yet)
Key
Tested
Built, not validated
Isolated (works alone)
Planned
works today
still to join, with task IDs
No end-to-end run yet, as planned. First full run (speak, look, drive, grasp) is M4, January 2027. The plan’s target for this interim was "M0 done, M1 and M3 under way"
Sherman
Notes: PRESENTER: Sherman SLOT: 1:05 ELAPSED AT END OF SLIDE: 17:10 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) Here is the full flow from slide 4 again, with each part we have just shown placed where it sits. Built and connected today: a recorded voice command starts a real grasp on the real arm, and since this week the glasses crop also chooses which object the arm goes for, on replayed recordings. My map feeds the navigation frame tree, and the memory graph is built from my recorded drive. Two links are still to join. The robot has to explore with a live memory graph, match what it sees against the gaze target, and turn a match into a navigation goal. Nav2 has to drive the base, which I start right after this presentation. So there is no end-to-end run yet. That matches the plan: the first closed-loop run is milestone M4, in January. Here is how we stand against that schedule. TRANSITION Straight into slide 16, same presenter. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [VERIFY: CR§1 says M4 is "scheduled 28 Dec 2026 to 17 Jan 2027 (PP §5.1)" but CR§0.2 and §0.6 forecast it 11 to 31 Jan 2027, re-estimated 24 Oct. This slide uses "January 2027", which fits both. Use the CR§0.6 dates on slide 16. The project plan also disagrees with itself: PROJECT_PLAN.md:414 forecasts 11 to 31 Jan, its §6.6 heading still says 28 Dec to 17 Jan] [ARTEFACT NEEDED: the final slide 15 diagram, drawn from the idea above (any member)]

## Slide 16: Ahead on memory and gaze, behind on calibration and driving, final dates unchanged
recess
exams, early Dec
break
buffer
oral
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
Week (week 1 = 14 Sep 2026)
M0 Build and run
done 24 Sep
M1 Arm picks something up
8 Nov
M2 Voice and gaze to arm
10 Jan
M3 Base navigates
10 Jan
M4 Closed loop
31 Jan
M5 Calibrated base camera
24 Jan
M6 Memory graph offline
31 Jan
M7 Graph drives the robot
28 Feb
M8 Gaze picks the instance
14 Mar
M9 Frontier scoring (optional)
21 Feb, if kept
M10 Demo and paper
21 Mar
today: interim 28 Oct
final report 28 Mar
actual to 24 Oct
forecast
optional, likely cut
Grey bands: no work or half speed. Bars that cross them are calendar time, not working time. Forecasts re-estimated on 24 Oct: estimates, not commitments
Against the September plan at week 7
Planned: M0 done, M1 and M3 under way
Actual: M0 done. M1 met on the simple path. M3 map and localisation done
Started early: M2 (voice and gaze to arm), M6 (memory graph), M8 (gaze picks the instance)
Behind: base camera calibration (M5) and drive-to-point (M3), one to two weeks
Each milestone has a written test, for example M2: two boxes, the arm picks the one you looked at, 3 times in 4. Full list in A10
Progress: 97 of 171 task rows done
Final report 28 Mar 2027 (week 28), oral weeks 30 and 31
Sherman
Notes: PRESENTER: Sherman SLOT: 1:10 ELAPSED AT END OF SLIDE: 18:20 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) This chart shows every milestone by week. Each one has a written test. For example, M2 is done when, with two boxes on the table, the arm picks the one you looked at three times out of four. Solid bars are work done so far, light bars are our forecast, and the grey bands are recess, exams and the winter break, when we are not working. Our September plan expected, at this point, only the build milestone finished and the arm and base under way. We have that. The build milestone closed in week two. The arm picks up a box on the simple path. My map and localisation are done. Three milestones started well ahead of their windows: voice and gaze to the arm, the memory graph, and the gaze-instance work. The memory graph should finish a week early. Two things are behind, and both are mine: calibrating the base camera, because the rig is not built yet, and the test drives, because bring-up has taken twice my estimates. They slip one to two weeks into January. M8 and the final dates do not move. The weeks after the break carry most of the integration: closed loop in January, the robot exploring in February, and the end-to-end trials in March. TRANSITION (Handover) "Zongzhe will cover what the plan costs and what could go wrong. TEAM REVIEW BEFORE THE TALK (not shown on the slide) [VERIFY: M1's forecast (8 Nov) depends on the AnyGrasp licence reply expected around 26 Oct. Update if it has changed] [VERIFY: an examiner may ask for the original September plan. It is in git at 1cde0ec:docs/PROJECT_PLAN.md §5.3. Keep it as appendix slide A7]

## Slide 17: Budget: SGD 1,500 for compute, approved. Risks are mostly schedule and shared hardware
Budget in SGD, approved, dated 5 Oct 2026
Approved
No. | Item | Cost per unit | Units | Total | Purpose
1 | Hardware GPU | 1,000.00 | 1 | 1,000.00 | Compute requirement
2 | API credits | 500.00 | 1 | 500.00 | Compute requirement (AI services)
 | Total |  |  | 1,500.00 | 
Why compute: one shared 16 GB GPU runs SAM 3, AnyGrasp, CLIP, Whisper and two language models for three people and CI. Batched SAM 3 alone peaks at 10.3 GiB. The full set has never run together
Risks and status
 | Risk | Status
● | AnyGrasp licence bound to a hardware ID | New licence requested, network ID pinned
● | Shared, throttled lab machine | Ongoing: CPU throttling, two silent hangs, disk 89 % full
● | No hardware stop on arm or base | Software stop tested, two people and the power button at every test
● | Graph duplicates from poor camera poses | Controlled: 8 to 3 duplicates, 0 false merges
● ongoing ● controlled
Cut order if late: M9 (smarter exploration order), without-gaze comparison, reasoning layer, graph pruning, two-stage trigger, fewer end-to-end trials
Zongzhe
Notes: PRESENTER: Zongzhe SLOT: 0:45 ELAPSED AT END OF SLIDE: 19:10 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) Our budget is small and approved: a thousand Singapore dollars for a GPU and five hundred for API credits for AI services, both for compute. The reason is concrete. Everything runs on one 16 gigabyte GPU in the lab, shared by the three of us and by the CI runner. Segmentation, grasping, CLIP, speech and two language models all need it, and the memory graph's segmentation alone peaks at over 10 gigabytes. We have never run them all at once. The main risks are about schedule and shared hardware. If time runs short, we have a cut list fixed in advance, and the paper's smarter exploration order goes first. The grasp model's licence is tied to a machine ID, and a new one is requested. The lab machine is shared and has hung twice. And neither the arm nor the base has a working hardware stop, so every motion test has two people and a hand on the power button. TRANSITION To close, what happens next and what we want you to remember. TEAM REVIEW BEFORE THE TALK (not shown on the slide) Note: currency confirmed SGD by Dion. The API credits are for AI services in general. The team explains the detail if asked. [TEAM INPUT REQUIRED: whether the GPU has been bought yet and any spend to date, in case an examiner asks]

## Slide 18: Next: close the grasp, drive the base, query the graph. Then explore with gaze
Weeks 7 to 8, before exams
Refuse weak gaze picks at the glasses, then the gaze-matched grasp on the real arm T2.24, T8.9a
New AnyGrasp SDK, fused-view retest, then a 12-trial grasp validation. M1 closes (target 8 Nov) T1.45, T1.47, T1.35
Nav2 prerequisites and the first drives to a point T3.6
Memory graph query acceptance run on the recorded drive T6.8
After the break, January to March 2027
Two-box gaze grasp on hardware (M2), camera calibration (M5) T2.5, T5.5, T5.6
Closed loop (M4, January) M4
The robot explores and finds the user (M7, February) T7.2, T7.5, T7.6, T7.1
A gaze match ends exploration, end-to-end trials (M8, March) T8.2, T8.3
Three takeaways
1
The hard part is identity across viewpoints. CLIP does it for different objects and now steers the grasp. Gaze geometry is needed for look-alikes
2
Every subsystem has measured results on real hardware or real recordings
3
The links are scheduled, with a cut list fixed in advance
1 Intent
2 Explore and map
3 Search
4 Approach and confirm
5 Grasp
March 2027: end-to-end demonstration
Zongzhe
Notes: PRESENTER: Zongzhe SLOT: 0:50 ELAPSED AT END OF SLIDE: 20:00 of 20:00 SCRIPT (approved, from INTERIM_PRESENTATION_SLIDE_CONTENT_2026-10.md) In the next two weeks, before exams, we close four specific gaps. The glasses learn to refuse a weak gaze pick, and the gaze-matched grasp runs on the real arm. The new AnyGrasp version and the fused views are tested, then a twelve-trial validation closes the grasp milestone. Sherman starts driving the base with Nav2. And I run the full memory graph query on the recorded drive, checked against the answer key. After the break, the pieces join: the two-box gaze test on the real arm, the camera calibrations, the first closed-loop run in January, and the robot exploring on its own in February, with a gaze match telling it when to stop. In March we run the end-to-end trials. Three things to take away. The hard part of this problem is keeping the object's identity across very different viewpoints. Every subsystem now has measured results on real hardware or real data. And the remaining links are scheduled, with a cut list fixed in advance. Thank you. We are happy to take questions. TRANSITION Into questions.

## Slide 19
Appendix
Backup slides for questions. Not part of the 20 minutes
A1 Topic-level wiring today
A2 Coordinate frames
A3 Matching rule and thresholds
A4 Grasp filters and the five options
A5 FAST-LIVO2 port defects and mid-route accuracy
A6 Limitations, risks and observed failures
A7 September plan vs now
A8 Why gaze, not just a class name
A9 End-to-end evaluation plan
A10 Milestone tests
Notes: Appendix divider. Backup slides for questions only.

## Slide 20: A1 Topic-level wiring today
Answers: "What exactly is connected?" Only links that exist in code. Grey rows exist in code but have not run
From | To | Channel | State
Voice: Silero VAD, faster-whisper, Qwen2.5-0.5B | aria_segmentation_client | /aria/audio/prompt (String) | Ran (replay)
Eye model | aria_segmentation_client | /aria/eye_tracking/gaze_estimate (PointStamped) | Ran (recording)
aria_segmentation_client, grasp_segmentation_client | SAM 3 service (one copy on GPU) | /segmentation/segment | Ran
aria_segmentation_client | grasp_segmentation_client | /grasp/target: word, then word plus reference crop | Ran on replay (T8.9a)
aria_segmentation_client | grasp_state_machine | /manipulator/grasp_request | Ran
grasp_segmentation_client | grasp_state_machine | /object_centroid_2d (pixel plus depth) | Ran
anygrasp_detection_node | grasp_state_machine | /grasp_candidates (state machine sends /pipeline_state back) | Ran
grasp_state_machine | MoveIt and rm_driver | real arm | Ran on the real arm
Livox MID-360, base D455 | FAST-LIVO2 (container) then fastlivo_odom_bridge | odom to robot_base_link | Ran live
fastlivo_odom_bridge | SLAM Toolbox, mapping mode | map to odom, /map | Ran live
SLAM Toolbox | Nav2 | frame tree | Never run on this
object_recognition_pipeline | object_approach_node | /manipulation/goal_pose (call site commented out) | Not run
object_approach_node | Nav2 | /goal_pose | Not run
Recorded drive handdriven1 | Memory graph S0 to S13, then TargetFinder | offline | Graph built. Query not run on the drive
Source: COMBINED_PROGRESS_REPORT_2026-10.md §3.3
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "What exactly is connected?" Only links that exist in code. Grey rows exist in code but have not run

## Slide 21: A2 Coordinate frames
Answers: "How do grasp poses reach the arm?"
map
odom
robot_base_link
livox_frame
base_link
Link1 to Link6
camera_link
camera_color_optical_frame
Parent to child | Published by | Value or note
map to odom | SLAM Toolbox | Nav2 plans in this map frame
odom to robot_base_link | Wheel driver, or the FAST-LIVO2 bridge (odom_source:=fastlivo) | Bridge: T_odom_base(t) = Tb x P0^-1 x P(t) x Tb^-1, Tb = (0.191, 0.02329, 0.15588) m. Refuses to start above 2 deg start tilt
robot_base_link to base_link | Static (arm mount) | (0.18, 0, 0.48) m, yaw 180 deg. Measured, tf2_echo matched
robot_base_link to livox_frame | Static | LiDAR mount
base_link through Link1..6 to camera_link | URDF | Wrist camera to arm calibrated (Dion, 2026-10-24)
camera_link to camera_color_optical_frame | RealSense driver | AnyGrasp candidates arrive in this frame
Frame question for later: FAST-LIVO2 publishes in camera_init and aft_mapped (its own TF is remapped to /fastlivo/tf). The memory graph stores positions in camera_init, Nav2 drives in SLAM Toolbox’s map. How graph positions reach map at run time is a design question for P2 and T7.1, not a defect
Source: COMBINED_PROGRESS_REPORT_2026-10.md §6.7, §5.4
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "How do grasp poses reach the arm?"

## Slide 22: A3 Matching rule and thresholds
Answers: "Why 0.56? Is CLIP cosine a probability?"
The rule (cross_camera_mask_match_rule.py)
Cosine of all pairs between each wrist mask crop (box plus 20 px) and the reference crop. Cutoff 0.56, tuned on 20 pairs (T8.7). Keep masks within 0.01 of the best. A wrist-side tie returns no match
Same model in both places: open_clip ViT-B-32 laion2b_s34b_b79k, 512-dimensional, L2-normalised
Not a probability
CLIP cosine is not a calibrated probability. Thresholds are empirical: 0.56 for the matcher, 0.6 on the graph’s combined score 1.5 x overlap + 0.5 x appearance (upstream weights)
float16 on the GPU shifts a vector by up to 0.0039 when batch size changes. Small against 0.56, but exact scores do not reproduce across batch sizes
Crop padding differs: glasses and wrist use box plus a fixed 20 px, the graph pads relative to the box
Where | Method | Confidence handling
Glasses mask | Gaze vote | Winner needs half the votes, else word only
Wrist mask (matcher) | CLIP cosine | Cutoff 0.56, wrist tie returns no match
Wrist mask (grasp) | CLIP cosine when a reference exists (T8.9a), else SAM 3 score | Cutoff 0.56 and no tie, else nothing published
Graph association | 3D overlap plus CLIP | Score over 0.6, greedy
Graph query | CLIP text vs image | Ranking only
No stage carries a confidence forward to the next (see A6)
Source: COMBINED_PROGRESS_REPORT_2026-10.md §5.4, §6.4, §6.6
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "Why 0.56? Is CLIP cosine a probability?"

## Slide 23: A4 Grasp filters and the five options
Answers: "Why not just lower the score floor?"
Filters on every AnyGrasp candidate (EXECUTING state)
On the SAM 3 mask
Inside the approach cone
Score at least 0.3
Width under 68 mm
Fingertips at most 45 mm past the near face
Pose stable for 5 frames
Of the 180 deg symmetric twins, the smaller wrist turn (T1.33)
Why the floor is not the fix: the top-down grasp scores at most 0.25, but the problem is the view. The 30 deg cone around the camera axis dropped every top-down grasp, because the camera axis is 44 deg from vertical. AnyGrasp was also used against its README: masked points only instead of the whole scene, 0.10 m width instead of the real one
Option | Idea | Cost
A. Grasp from the view pose | AnyGrasp once at 0.4 to 0.5 m with the whole box in view, one planned motion. Steps only as a fallback | Small. The pieces exist
B. Fused views (T1.47) | Several views in one cloud, grasp on that | Built, retest owed
C. New AnyGrasp SDK (T1.45) | Native mask and angle steering | Waiting on licence
D. Closed-loop tracking | AnyGrasp’s tracking mode updates the grasp while the arm moves | Medium. Old tracker node parked
E. Two-phase (shelved, T1.33) | Move to just before the depth blind zone, set the angle, then a straight move in and close | Small
[INSERT OPTIONAL: RVIZ GRASP RECORDING]
rviz_grasp_<date>.mp4, if Dion records it
Owner: Dion
Source: COMBINED_PROGRESS_REPORT_2026-10.md §5.5. Options: DION_PROGRESS_REPORT_2026-10.md §7 (options marked [inferred])
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "Why not just lower the score floor?"

## Slide 24: A5 FAST-LIVO2 port defects and mid-route accuracy
Answers: "How do you know the map is right?"
Defect (found by reading the source, confirmed against a control run) | Before | After the fix
Range gate cannot act (F2): blind_sqr never assigned, the port dropped upstream’s line | Median 19,968 points per scan, the full packet | Median 9,607. Removed fraction 0.5206 against 51.84 % audited zero-range points
LiDAR to IMU offset has the wrong sign (F3) | About 10.2 cm of geometric inconsistency in every replay before 19 Oct | Configs carry (-0.011, -0.02329, 0.04412) m. handdriven1 recorded after the fix
Voxel key mismatch: insertion and retrieval used different arithmetic for negative coordinates | Key hits 1,392,458 against 1,878,707 shadow hits | Hits match, 1,855,269. Accepted retrieval points 112,980 to 128,385
Mid-route accuracy (T3.5f)
Against the handdriven1 map as an independent reference, with the 0.15 s lag removed: within 6.7 cm (run 1) and 6.5 cm (run 2) for the whole route. Uncorrected 12.7 and 11.3 cm. The reference carries about 7 cm of its own error, so 6.7 cm is at the floor
The mapper stamps its pose about 0.15 s after the scan. Surfaces smear by speed x 0.15 s, about 4 cm at 0.28 m/s. Fix prepared, off by default (stamp_offset_s)
Floor marks did not close as ground truth (AB +0.264 m, BC 0.33 m too long). A tape-measured check is owed
[INSERT DRIFT PLOT: ERROR VS TIME]
nav_t35f_drift_step3_error_vs_time_2026-10-21.png
Owner: Sherman
Source: COMBINED_PROGRESS_REPORT_2026-10.md §8.4. SHERMAN_PROGRESS_REPORT_2026-10.md §9.3, §11.4, §11.5
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "How do you know the map is right?"

## Slide 25: A6 Limitations (1 of 3): confirmed in the implementation
Answers: "What fails today?" Most are links the plan schedules for later milestones
Limitation | End-to-end implication
A wrong gaze pick becomes a confident reference (T8.9a replay: at 1.5 m the reference was the mat, the other box scored just over 0.56 twice) | The arm would go for the wrong box if a grasp request were open. T2.24 refuses weak gaze picks
/manipulation/goal_pose has no live publisher (inherited) | Nothing can start navigation to an object yet. T7.1 will publish it
No graph query service, no T7.1 node | The graph cannot drive the robot
No gaze-target trigger on graph objects | The exploring robot cannot yet tell it has found the target. Glasses crop vs base-camera features is untested
Graph built offline from a hand-pushed recording | No live graph. No depth camera data
No calibration between any cameras | Graph positions and the gaze ray carry unknown rotation error. About 6.7 px per degree on the base camera
Software-only stops on arm and base | Every hardware test needs two people and the power button
No automatic grasp success check | Outcome must be judged by people. A retry loop cannot know when to retry
Source: COMBINED_PROGRESS_REPORT_2026-10.md §9.1
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "What fails today?" Most are links the plan schedules for later milestones

## Slide 26: A6 Limitations (2 of 3): architectural risks to test
Answers: "What could break when the parts join?"
Risk | What to watch
No confidence crosses a stage boundary | A wrong gaze pick gives a confident reference, a wrong graph hit gives a goal, a wrong wrist mask gives a grasp. The matcher caught one wrong reference by luck of score (0.51 vs 0.56)
Crop mismatch | Fixed 20 px glasses crop against the graph’s relative padding, when the gaze match (P3) lands
Frame of graph positions | camera_init against Nav2’s map frame, to settle when P2 and T7.1 are built
Standoff vs reach | 0.6 m camera standoff against the 35 to 46 cm tested grasp band, to check at the first nav-to-object test
GPU contention | SAM 3 service, batched graph SAM 3 (up to 10.3 GiB), AnyGrasp, CLIP, Whisper, two Qwen models on one 16 GB card. Never run together
0.15 s pose lag | Anything pairing a scan with a pose by stamp, including graph depth if rendered that way
Viewpoint change between graph and wrist | Graph features from the base camera at knee height, reference from the glasses, confirmation from the wrist. Glasses to base camera is untested
Source: COMBINED_PROGRESS_REPORT_2026-10.md §9.3
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "What could break when the parts join?"

## Slide 27: A6 Limitations (3 of 3): observed failures
Answers: "What has gone wrong on hardware or data?"
Failure | Where | Source
AnyGrasp’s confident grasps are across the too-wide face. Fit check passes edge slices | Wrist, 0.21 m | T1.44
Live OK-Robot trials 0 of 4: one pushed the box, two stuck in EXECUTING, one found nothing in 3 s | Real arm | T1.44
Wrist spun 180 deg and knocked the box off (fixed) | First AnyGrasp grasp | T1.33
Wide wrist twist (j4 146, j5 29, j6 274 deg) | AnyGrasp grasp B | T1.40
Look-alike boxes: 148 of 180, 6 of 12 | Matcher | T8.5, T8.8
Gaze landed on the mat stack at 1.5 m | Glasses | T8.5
Keypoint matching 0 of 15 | Cross camera | T8.4
Mapper teardown aborts 2 of 4. LiDAR driver SIGBUS | Base | S§10.3
Ethernet flap caused 8.1 s and 15.1 s IMU time jumps | Base, live | T3.5d
Lab box silent hangs (2026-10-06, 2026-10-20) | Shared box | S§15
Glass walls: about 42 % of 5 cm map points are ghosts outside the glass box | Map | S§15
Glass door and both computer towers missed in every graph setting | Graph | Z§3.5
Lab visitors’ faces appear in Sherman’s coloured map. Cleared for this internal presentation. Re-render before any external showing
Source: COMBINED_PROGRESS_REPORT_2026-10.md §9.2. 148 of 180 (T8.5, matcher on display) is not the same count as 266 of 268 on slide 12 (T8.9a, published targets only)
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "What has gone wrong on hardware or data?"

## Slide 28: A7 September plan vs now
Answers: "How does this compare with your original plan?"
Milestone | September plan window | Now (actual to 24 Oct, forecast end) | Change
M0 Everyone can build and run | 14 to 27 Sep 2026 | Done 24 Sep | On time
M1 The arm picks something up | 5 Oct to 1 Nov 2026 | Started 21 Sep. Forecast 8 Nov | About one week later (AnyGrasp)
M2 Voice and gaze reach the arm | 26 Oct 2026 to 3 Jan 2027 | Started 8 Oct. Forecast 10 Jan | Started early, ends about one week later
M3 The base navigates | 12 Oct to 27 Dec 2026 | Started 14 Sep. Forecast 10 Jan | Two weeks later
M4 Closed loop | 28 Dec 2026 to 17 Jan 2027 | Forecast 11 to 31 Jan | Two weeks later
M5 Calibrated base camera | 5 Oct 2026 to 17 Jan 2027 | Started 16 Sep. Forecast 24 Jan | One week later
M6 Memory graph offline | 28 Dec 2026 to 7 Feb 2027 | Started 21 Sep. Forecast 31 Jan | One week earlier
M7 The graph drives the robot | 1 to 28 Feb 2027 | Forecast 18 Jan to 28 Feb | Can start earlier, end unchanged
M8 Gaze picks the instance | 8 Feb to 14 Mar 2027 | Started 19 Oct. Forecast 14 Mar | Started early, end unchanged
M9 Frontier scoring (optional) | 2 Nov 2026 to 21 Feb 2027 | Not started. 18 Jan to 21 Feb if kept | First on the cut list
M10 Demonstration and paper | 1 to 21 Mar 2027 | Forecast 1 to 21 Mar | Unchanged
September plan windows from the milestone headings of the plan in git at 1cde0ec:docs/PROJECT_PLAN.md. Its §6.6 heading gives M4 as 28 Dec to 17 Jan, while PROJECT_PLAN.md:414 forecasts 11 to 31 Jan
Source: 1cde0ec:docs/PROJECT_PLAN.md §5 and §6 headings. COMBINED_PROGRESS_REPORT_2026-10.md §0.2, §0.6
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "How does this compare with your original plan?"

## Slide 29: A8 Why gaze, not just a class name
Answers: "Isn’t identical-object picking niche?"
Two truly identical objects are the hardest test case, not the pitch.
The capability is knowing where the user is looking in the robot’s own 3D space
Similar objects
Two chairs of the same model score 0.81 to 0.85 in CLIP, close to the same chair at 0.93
Partly hidden objects
The robot may see only part of the object the user sees
Uncertain image features
Appearance alone is not a reliable identity
A robot that does not see what the user sees
The base camera is at knee height, the glasses at eye level
Assistive use
A user who can look but cannot easily point or speak, in a scene full of mugs, pill bottles and cans
Source: COMBINED_PROGRESS_REPORT_2026-10.md §0.3 (D§5.5). CLIP values: §8.5
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "Isn’t identical-object picking niche?"

## Slide 30: A9 End-to-end evaluation plan
Answers: "How will you measure the final system?" Today every measurement is per stage, none end to end
Metric | Definition | Needs | Milestone
Glasses target accuracy | Reference crop is the intended object, per spoken command, scenes with 2 to 4 objects at 1 to 3 m | Live glasses | M2
Wrist confirmation accuracy | Matcher picks the intended object, with and without look-alikes. Refusals counted apart from wrong picks | P0 item 1 | M2
False acceptance rate | Wrong object accepted, per stage (glasses, graph, wrist) | Labelled trials | M2, M8
Graph target retrieval | First hit lands on the intended marked object, and distance to it | T6.8 | M6
Gaze-target trigger accuracy | The robot stops exploring at the intended object. Wrong stops and wrist rejects counted | T8.2 | M8
User discovery and search distance | User found, and distance driven before the target is matched | T7.5, T7.6 | M7
Without gaze (stretch) | Same trials, voice only | T8.11 | M8
Drive-to-point repeatability | Ten drives, landing error, 10 cm circle | T3.6, T5.8 fixture | M3
Handover success | Base stops with the object inside the grasp band | T3.7 | M4
Grasp success | 12-trial grid, pass bar 9 of 12 | T1.35 | M1
End-to-end success | Speak, look, drive, grasp. Counted only when the intended object is lifted | All above | M4, M10
Per-stage timing | 99th percentile per stage | T4.2 | M4
Recovery | Share of failures that end safely (refusal, ask, reject and retry) instead of a wrong grasp | P1 items | M4
Source: COMBINED_PROGRESS_REPORT_2026-10.md §11
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "How will you measure the final system?" Today every measurement is per stage, none end to end

## Slide 31: A10 Milestone tests
Answers: "How do you know a milestone is done?"
 | Milestone | Done means | Lead
M0 | Everyone can build and run | Two people other than Dion clone, build and pass the bench | Zongzhe
M1 | Arm picks something up | 5 grasp attempts on a box, success rate recorded, stop verified first | Dion
M2 | Voice and gaze reach the arm | Two boxes, the arm picks the one you looked at, 3 times in 4 | Dion
M3 | Base navigates | Map, localisation, ten drives to a point with error recorded | Sherman
M4 | Closed loop | One recorded run: speak, look, drive, grasp, per-stage timing | Dion
M5 | Calibrated base camera | LiDAR points land on the right objects in the camera image, pose error as a number | Sherman mount, Dion calibration
M6 | Memory graph offline | Objects from a recorded drive, no duplicates, a sentence query returns the right one | Zongzhe
M7 | Graph drives the robot | Object out of view: the robot explores, finds the user, builds the graph live, drives to the object | Dion
M8 | Gaze picks the instance | A gaze match ends exploration. N end-to-end trials, success per phase | Dion
M9 | Smarter exploration order (optional) | The paper’s exploration order beats our nearest-first exploration | Zongzhe
M10 | Demonstration and paper | Recorded end-to-end run, paper whose central table is the end-to-end trials | All
Source: COMBINED_PROGRESS_REPORT_2026-10.md §0.2
Notes: BACKUP SLIDE, not in the 20 minutes. Answers: "How do you know a milestone is done?"